## Slide 1: Boot File of Pandaboard
Noritsuna Imamura
noritsuna@siprop.org

## Slide 2: Download & Build u-boot
Download it with Patch of Boot Option
  cd ~/panda_work
  git clone git://git.omapzoom.org/repo/u-boot.git
  cd u-boot
  git checkout -b omap4_dev origin/omap4_dev
  wget http://android-development-environment.googlecode.com/files/0001-change-bootarges.patch
  git apply 0001-change-bootarges.patch
  make omap4430panda_config
  make
  cp -a u-boot.bin ~/panda_work/mydroid/device/ti/panda/bootloader.bin
Notes: 吸出xīchū,抽出chōuchū

## Slide 3: About boot.scr
Contents of Patch
  --- a/include/configs/omap4430panda.h
  +++ b/include/configs/omap4430panda.h
  @@ -147,8 +147,7 @@
  " ip=dhcp"
  #else
  -#define CONFIG_BOOTARGS "console=ttyO2,115200n8 mem=512M" \
  - " init=/init vram=32M omapfb.vram=0:16M androidboot.console=ttyO2"
  +#define CONFIG_BOOTARGS "kgdboc=ttyO2,115200 console=ttyO2,115200n8 mem=1G androidboot.console=ttyO2"

## Slide 4: About boot.scr
If you want to change boot option by script file
  Sample of Boot Script file: File Name=boot.txt
  How to Make boot.scr from Boot Script file
    mkimage -A arm -T script -O linux -C none -a 0 -e 0 -n "boot.scr" -d boot.scr.txt boot.scr
  setenv fdt_high "0xffffffff"
  setenv bootcmd "fatload mmc 0:1 0x80200000 uImage; fatload mmc 0:1 0x81600000 uInitrd; fatload mmc 0:1 0x815f0000 board.dtb; bootm 0x80200000 0x81600000 0x815f0000"
  setenv bootargs "console=ttyO2,115200n8 rootwait ro earlyprintk fixrtc nocompcache vram=48M omapfb.vram=0:24M,1:24M mem=456M@0x80000000 mem=512M@0xA0000000 init=/init androidboot.console=ttyO2 omapfb.mode=dvi:1280x800MR-24@60 consoleblank=0"

## Slide 5: Common Setup 1/2
Setup Build Tools
  sudo apt-get install
    bison build-essential curl flex git-core gnupg gperf libesd0-dev libncurses5-dev libsdl1.2-dev libwxgtk2.8-dev libxml2 libxml2-utils lzop openjdk-6-jdk openjdk-6-jre pngcrush schedtool squashfs-tools xsltproc zip zlib1g-dev
    g++-multilib gcc-multilib lib32ncurses5-dev lib32readline-gplv2-dev lib32z1-dev
Setup Build Tools for ARM
  sudo apt-get install
    uboot-mkimage
Notes: 共通gòngtōng
安装ānzhuāng
工具gōngjù