## Slide 1: What’s Making Android?
Noritsuna Imamura
noritsuna@siprop.org

## Slide 2: Agenda
What’s Android System?
  Kinds of Android Devices
  Kinds of Android Type
  Android Source Code
Inside Android
  Boot Sequence
  About init File
Hands On
  Nexus7
  Pandaboard
  How to Debug
Appendix
  How to Build Android Source Code for Other Devices
Notes: という形で進める

## Slide 3: Kinds of Android Device
Smart Phone
Tablet
Mini PC
Note PC
Car Navigation
Set Top Box
Smart Watch
Smart Glass
Camera
Game Console
Audio System
Micro Wave
Refrigerator
Cut Board
EVB
If you get today’s knowledge,
You can customize these devices yourself!!!

## Slide 4: Why Customize it?
More Functions
  Add Other Library
  Add Other Software
Attach Other Device
  Add Driver
So Slow(Ex. Old PC)
  Modify Bottleneck Software
  Delete needless Software & Library
Useless
  Customized UI/UX Software

## Slide 5: Kinds of Android Type
Android | Kernel | More Functions | Attach Other Device | So Slow | Useless
No Source | No Source | × | × | × | ×
No Source | w/Source | × | △ No-Use as Android App | △ | ×
w/Source | No Source | ○ | × | ○ Almost Bottleneck In Here | ○ UI/UX Engine In Here
w/Source | w/Source | ◎ Use Kernel Level Driver | ○ | ◎ | ○

## Slide 6: About Android
Android Framework has 3 Layer Stack for SmartPhone & Tablet PC.
  Application Framework Layer (Java)
  Library Layer (Linux C/C++)
  Kernel/Driver Layer (Linux Kernel C/ASM)

## Slide 7: About Android Source Code
  packages
    App for Android
  frameworks
    Lib for Android Apps
  system
    Sys Lib for Framework
  docs
    Java Doc for Android
  developers
    Sample, Demos
  build
    Tool for Android Build
  prebuilts
    Toolchain
  sdk
    Android SDK
  ndk
    Native SDK
  pdk
    for 3rd Party SDK
  cts
    Compatibility Test
  tools
    Tools for External

## Slide 8: About Android Source Code
  external
    Linux Lib
  libcore
    Lib for Android
  bionic
    libc for Android
  libnativehelper
    Helper for JNI
  abi
    Application Binary Interface
  dalvik
    Java VM
  art
    Next Generation VM
  device
    Diff for Devices
  hardware
    Drivers
  bootable
    BootLoader

## Slide 9: License
3 Types License
  Apache 2.0
    All Application Framework
    Some Libraries
      Bionic
  GPL
    Almost Libraries
    Linux Kernel
  Google Proprietary
    Google Applications from Play Store
      How to Get Play Store?
        Pass CTS
Apache 2.0
GPL
Google Proprietary
Google Android
AOSP
(Android Open Source Project)

## Slide 10: GApp
Goo.im – Premium Android Developer File Hosting
  This Site hosts Google Proprietary Apps!!!
    http://goo.im/home
  You can use Google Proprietary Apps on your Device.
    However it’s illegal…

## Slide 11: Feature Matrix of ARM Chips
 | AllWinner | RockChip | MediaTek | Freescale | TI | Samsung | Qualcomm
Chip Name | A31 | RK3188 | MT6589 | i.MX6Q | OMAP5432 | Exynos5 | Krait400
CPU Type | A7 Quad | A9 Quad | A7 Quad | A9 Quad | A15 Dual | A15 Quad | A15 Quad
Device Type | Tablet | Mini PC | Smart Phone | EVB | EVB | EVB | Tablet
Used Area | Cheap Device | Cheap Device | Cheap Phone | N/A | Customized Device | N/A | 3G/LTE Device
Official Source Code | Kernel | Kernel | Some Android Kernel | Full Android Kernel | Full Android Kernel | Full Android Kernel | Full Android Kernel
Support | × | △ | × | ○ | ◎ | ◎ | ○
Availability | ○ | ○ | ？ | ◎ | ◎ | ？ | ×
Promising | ○ | ◎ | ○ | × | × | ○ | △
Reason | Cheapest | Better chip | RF chip |  | Dev team is gone |  | Expensive
Notes: 机能[jīnéng]
图表[túbiǎo]
正式zhèngshì
源代碼
支持zhīchí
[有用性]yǒuyòngxìng
有前途yǒu qiántú

## Slide 12
Inside Android
Notes: 共通gòngtōng
安装ānzhuāng

## Slide 13: Boot Up Flow CPU～Kernel
Ex. x-loader&u-boot

## Slide 14: Boot Up Flow Kernel～Android System
Init
  Set Permission
  Mount Disks
  Load Driver
Demons
  Linux App
Zygote
  Sharing JavaResource Manager
Runtime
  Linux SO
  Driver

## Slide 15: About init File
What’s works?
  Prepare dir, file for Service
  Run Services(Demon), Runtime
  Setup Permission
  on post-fs-data
  mkdir /data/media 0770 media_rw media_rw
  setprop vold.post_fs_data_done 1
  mkdir /data/misc/dhcp 0770 dhcp dhcp
  chown dhcp dhcp /data/misc/dhcp
  mkdir /data/misc/wifi/sockets 0770 wifi wifi
  service dhcpcd_wlan0 /system/bin/dhcpcd -ABKL
  disabled
  oneshot
  #for V4L
  /dev/video0 0666 system system
  /dev/video1 0666 system system

## Slide 16: Difference of Between Linux to Android

## Slide 17: Sorry!!!
About SMP(Multi Core) Compile
  Next Week!

## Slide 18
Hands On
Notes: 共通gòngtōng
安装ānzhuāng

## Slide 19: Setup 2 Kinds of Android
SmartPhone
  Nexus7 (2013)
  Android 4.3
    Released by Community
      Non-Driver(BSP)
EVB
  Pandaboard
  Android 4.4
    Released by Google
      All Softwares

## Slide 20: Building Environment
CPU
  Core i7
    4core – 8thread
Memory
  8GB
OS
  Ubuntu12.04 64bits
Notes: 编译[biānyì]
记忆jìyì
螢幕(ying mu)

## Slide 21
Common Setup
Notes: 共通gòngtōng
安装ānzhuāng

## Slide 22: Common Setup 1/2
Setup Build Tools
  sudo apt-get install
    bison build-essential curl flex git-core gnupg gperf libesd0-dev libncurses5-dev libsdl1.2-dev libwxgtk2.8-dev libxml2 libxml2-utils lzop openjdk-6-jdk openjdk-6-jre pngcrush schedtool squashfs-tools xsltproc zip zlib1g-dev
    g++-multilib gcc-multilib lib32ncurses5-dev lib32readline-gplv2-dev lib32z1-dev
Setup Build Tools for ARM
  sudo apt-get install
    uboot-mkimage
Notes: 共通gòngtōng
安装ānzhuāng
工具gōngjù

## Slide 23: Common Setup 2/2
Setup Build Tools for Android
  curl http://commondatastorage.googleapis.com/git-repo-downloads/repo > ~/bin/repo
  chmod a+x ~/bin/repo
  export PATH=$PATH:~/bin/repo
  sudo add-apt-repository ppa:nilarimogard/webupd8
  sudo apt-get update
  sudo apt-get install android-tools-fastboot
Notes: 下载xiàzài

## Slide 24
Nexus7

## Slide 25: What’s Nexus7?
Target
  Tablet
    Nexus7(2013)
      http://www.google.com/nexus/7/
OS
  JCROM
    With Build Manual
    https://sites.google.com/site/jcromproject/

## Slide 26: Check Points
How to Customize Community Source Code
  How did they get them?
    They don’t have BSP(Driver).
  How about Android System.
    eMMC, OTA-Package
You can Customize GUI(HOME)
  What can you Customize Android System?
    UI System, Settings

## Slide 27: How to Build
Setup Process
  Download Source Code
  Download BSP from site & your real device
  Download & Build kernel
  Make OTA image
  Write new OTA image

## Slide 28: Download Source Code
Download from JCROM’s repository
  repo init -u https://bitbucket.org/sola/jcrom_manifest -m jcrom_jb-4.3-master.xml
  repo sync

## Slide 29: Download BSP from site & your real device 1/2
Register your board to udev.
  Add the following line to ‘/etc/udev/rules.d/51-android.rules’
  Restart ‘udev’ service
  SUBSYSTEM=="usb", ATTR{idVendor}=="18d1", ATTR{idProduct}=="4e40", MODE="0666" # Bootloader
  SUBSYSTEM=="usb", ATTR{idVendor}=="18d1", ATTR{idProduct}=="d001", MODE="0666" # Recovery
  SUBSYSTEM=="usb", ATTR{idVendor}=="18d1", ATTR{idProduct}=="4e43", MODE="0666" # PTP media, USB debug off
  SUBSYSTEM=="usb", ATTR{idVendor}=="18d1", ATTR{idProduct}=="4e44", MODE="0666" # PTP media, USB debug on
  SUBSYSTEM=="usb", ATTR{idVendor}=="18d1", ATTR{idProduct}=="4e41", MODE="0666" # MTP media, USB debug off
  SUBSYSTEM=="usb", ATTR{idVendor}=="18d1", ATTR{idProduct}=="4e42", MODE="0666" # MTP media, USB debug on
  SUBSYSTEM=="usb", ATTR{idVendor}=="18d1", ATTR{idProduct}=="4ee2", MODE="0666" # MTP media, USB debug on

## Slide 30: Download BSP from site & your real device 2/2
Download BSPs from Real Device & Internet
  *This version uses Internet only.
  Use adb
    If your system doesn’t have adb, please do:
      sudo apt-get install android-tools-fastboot
  cd ~/nexus_work/android/device/asus/flo
  ./download-blobs.sh
  cd ~/nexus_work/android/jcrom/asus/flo/proprietary/
  ./extract-files.sh
Notes: 吸出xīchū,抽出chōuchū

## Slide 31: Download & Build kernel
Download & Build kernel
  cd ~/nexus_work
  export ARCH=arm
  export CROSS_COMPILE=~/nexus_work/android/prebuilts/gcc/linux-x86/arm/arm-eabi-4.6/bin/arm-eabi-
  git clone https://android.googlesource.com/kernel/msm.git -b android-msm-flo-3.4-jb-mr2 kernel/nexus72
  cd kernel/nexus72
  make flo_defconfig
  make
  cp arch/arm/boot/zImage ~/nexus_work/android/device/asus/flo-kernel/kernel

## Slide 32: Make OTA image
Make OTA image
  This OTA image is update image for Android.
  This file name is
    aosp_flo-ota-eng.[your Linux’s User name].zip
  cd ~/nexus_work/android/
  source build/envsetup.sh
  lunch aosp_flo-user
  make otapackage

## Slide 33: build/envsetup.sh
Helper Command Lib for Android Build
  m
    Build from Top Dir
  mm
    Build from Current Dir
  mmm [Target Dir]
    Build from Target Dir
  croot
    Change Top Dir
  cgrep
    Grep for C/C++ Source Code
  jgrep
    Grep for Java Source Code
  resgrep
    Grep for XML Source Code
  lunch
    Choose Target Build

## Slide 34: What’s Android OTA-Package
OTA = Over-The-Air (Update)
Android OTA-Package has ROM images.
  boot.img
    Kernel, Init, Minimam Linux
  cache.img
    Temporary Area
  recovery.img
    Recovery Manager Program
  system.img
    Android System
  userdata.img
    User Data

## Slide 35: What’s Fastboot?
Fastboot is ROM Manager for eMMC.
  eMMC is managed by Address in Low Lovel.
    When you write your Kernel, you MUST point kernel address.
    If you mistake kernel address, your system is broken…
Separated by Address

## Slide 36: What’s Inside of Image File?
It’s ramdisk
  boot.img-ramdisk.gz
  If your new kernel has new functions, please modify ramdisk files.
    Ex. .ko file, new init file, etc.
  mkdir ramdisk
  cd ramdisk
  gunzip -c ../boot.img-ramdisk.gz | cpio –I
Notes: 打開

## Slide 37: Write new OTA image 1/3
If your phone has OEM lock, please unlock it.
Change Recovery image.
※Connect your N7 to PC
  adb reboot bootloader
  fastboot oem unlock
  wget http://download2.clockworkmod.com/recoveries/recovery-clockwork-6.0.4.3-flo.img
  fastboot flash recovery recovery-clockwork-6.0.4.3-flo.img
  fastboot boot recovery-clockwork-6.0.4.3-flo.img

## Slide 38: Write new OTA image 2/3
Push your new OTA image to your N7
If you want to use Google Apps
※Connect your N7 to PC
  adb push ~/nexus_work/android/out/target/product/flo/aosp_flo-ota-eng.[your Linux's User name].zip /sdcard/
  wget http://goo.im/gapps/gapps-jb-20130813-signed.zip
  adb push gapps-jb-20130813-signed.zip /sdcard/

## Slide 39: Write new OTA image 3/3
Turn off your phone
Volume Up & Power
Wipe data/factory reset
Install zip from sdcard
Choose zip from sdcard
aosp_flo-ota-eng.[your Linux's User name].zip
Choose zip from sdcard
gapps-jb-20130813-signed.zip
+++++Go Back+++++
Reboot system now

## Slide 40
Boot up Your Nexus7!

## Slide 41
Pandaboard

## Slide 42: What’s Pandaboard?
Target
  EVB
    Pandaboard
      http://www.pandaboard.org/
OS
  Official Kernel & Android
    With Build Manual
    http://source.android.com/source/downloading.html

## Slide 43: How to Use Peripherals?
ADK (Accessory Development Kit)
  http://developer.android.com/tools/adk/index.html
Advantage
  Develop on ADT
  Pin like Arduino
Dis-Advantage
  So Slow…
    9600bps

## Slide 44: How to Use Peripherals?
GPIO(General Purpose Input/Output)
  I2C(Inter-Integrated Circuit)
  SPI(Serial Peripheral Interface)
  UART(Serial)
    Fast: SPI > I2C
    Pin Num: SPI(4Pins) > I2C(3Pins)
    GPIO can use Registers.
Advantage
  Bus Speed
  Connect All Peripheral
Dis-Advantage
  Required Hardware Knowledge
    Like Assembler for Hardware

## Slide 45: How to Build
Setup Process
  Download Source Code
  Download BSP from Google
  Download & Build Boot Loaders
  Build Android
  Setup SD Card

## Slide 46: Download 4.4 Source Code
Download from AOSP(Google)’s repository
  mkdir ~/panda_work
  cd ~/panda_work
  mkdir mydroid
  cd mydroid
  repo init -u https://android.googlesource.com/platform/manifest -b android-4.4_r1.1
  repo sync

## Slide 47: Download BSP from Google
Download BSPs(Driver)
  cd ~/panda_work/mydroid
  wget https://dl.google.com/dl/android/aosp/imgtec-panda-20130603-539d1ac3.tgz
  tar zxvf imgtec-panda-20130603-539d1ac3.tgz
  ./extract-imgtec-panda.sh
  git clone https://github.com/sola-dolphin1/sola_device_ti_panda.git -b kitkat device/ti/panda
Notes: 吸出xīchū,抽出chōuchū

## Slide 48: Download Toolchain
Required Android Toolchain for Panda’s Source
  cd ~/panda_work
  git clone https://android.googlesource.com/platform/prebuilt
  export ARCH=arm
  export CROSS_COMPILE=$PWD/prebuilt/linux-x86/toolchain/arm-eabi-4.4.3/bin/arm-eabi-
Notes: 吸出xīchū,抽出chōuchū

## Slide 49: Download & Build x-loader
First Boot Loader for Pandaboard
  cd ~/panda_work
  git clone git://git.omapzoom.org/repo/x-loader.git
  cd x-loader
  git checkout -b omap4_dev origin/omap4_dev
  make omap4430panda_config
  make ift
  cp -a MLO ~/panda_work/mydroid/device/ti/panda/xloader.bin
Notes: 吸出xīchū,抽出chōuchū

## Slide 50: Download & Build u-boot
Second Boot Loader for Pandaboard
  cd ~/panda_work
  git clone git://git.omapzoom.org/repo/u-boot.git
  cd u-boot
  git checkout -b omap4_dev origin/omap4_dev
  wget http://android-development-environment.googlecode.com/files/0001-change-bootarges.patch
  git apply 0001-change-bootarges.patch
  make omap4430panda_config
  make
  cp -a u-boot.bin ~/panda_work/mydroid/device/ti/panda/bootloader.bin
Notes: 吸出xīchū,抽出chōuchū

## Slide 51: Download & Build kernel
Kernel for Pandaboard
  cd ~/panda_work
  git clone https://android.googlesource.com/kernel/omap.git kernel
  cd kernel
  git checkout -b android-omap-panda-3.0 origin/android-omap-panda-3.0
  make panda_defconfig
  make
  cp -a arch/arm/boot/zImage ~/panda_work/mydroid/device/ti/panda/kernel
Notes: 吸出xīchū,抽出chōuchū

## Slide 52: Build Android
Build Android
  cd ~/panda_work/mydroid
  source build/envsetup.sh
  lunch aosp_panda-userdebug
  make
Notes: 吸出xīchū,抽出chōuchū

## Slide 53: Setup SD Card
Make Partition for Android on SD Card
  boot
  system
  cache
  userdata
  media
  wget http://www.noritsuna.com/download/mksdcard_pandaboard.sh
  chmod a+x mksdcard_pandaboard.sh
  LANG=C sudo ./mksdcard_pandaboard.sh /dev/sdX ~/panda_work/mydroid
Notes: 吸出xīchū,抽出chōuchū

## Slide 54
Boot up Your Pandaboard!

## Slide 55: But……… TI support until 4.2
2012.06.27 4.1 Jelly Bean
2012.11.13 4.2
2013.07.24 4.3
4.3
  Support OpenGL/ES 3.0
  Support Bluetooth LE
  Support Wi-Fi Location
  Linux: 3.4.0
4.1, 4.2
  Available USB Audio
  Support i18n(Internationalization)
  Support Vibration for Input Device
  Support Miracast
  Support Writing Vertically
  Support RenderScript
  Change Android Market to Google Play
  Linux: 3.1.10

## Slide 56: How to Build
Setup Process
  Download Source Code
  Download BSP from Google
  Download & Build Boot Loaders
  Build Android
  Setup SD Card

## Slide 57: Download 4.2 Source Code
Download from AOSP(Google)’s repository
  mkdir ~/panda_work
  cd ~/panda_work
  mkdir mydroid
  cd mydroid
  repo init -u https://android.googlesource.com/platform/manifest -b android-4.2.1_r1
  repo sync

## Slide 58: Download BSP from Google
Download BSPs(Driver)
Get some Patches
  cd ~/panda_work/mydroid
  wget https://dl.google.com/dl/android/aosp/imgtec-panda-20120807-c4e99e89.tgz
  tar zxvf imgtec-panda-20120807-c4e99e89.tgz
  ./extract-imgtec-panda.sh
  cd ~/panda_work/mydroid/build/
  wget http://sola-dolphin-1.net/data/Panda/0001-panda-jb4.2_build.patch
  git apply 0001-panda-jb4.2_build.patch
  cd ~/panda_work/mydroid/device/ti/panda/
  wget http://sola-dolphin-1.net/data/Panda/0001-panda-jb4.2_device-ti-panda.patch
  git apply 0001-panda-jb4.2_device-ti-panda.patch
  cd ~/panda_work/mydroid/hardware/ti/omap4xxx/
  wget http://sola-dolphin-1.net/data/Panda/0001-panda-jb4.2_hardware-ti-omap4xxx.pah
  git apply 0001-panda-jb4.2_hardware-ti-omap4xxx.patch
  cd ~/panda_work/mydroid/hardware/ti/wpan/
  wget http://sola-dolphin-1.net/data/Panda/0001-panda-jb4.2_hardware-ti-wpan.patch
  git apply 0001-panda-jb4.2_hardware-ti-wpan.patch
Notes: 吸出xīchū,抽出chōuchū

## Slide 59: Download Toolchain
Required Android Toolchain for Panda’s Source
  cd ~/panda_work
  git clone https://android.googlesource.com/platform/prebuilt
  export ARCH=arm
  export CROSS_COMPILE=$PWD/prebuilt/linux-x86/toolchain/arm-eabi-4.4.3/bin/arm-eabi-
Notes: 吸出xīchū,抽出chōuchū

## Slide 60: Download & Build x-loader
First Boot Loader for Pandaboard
  cd ~/panda_work
  git clone git://git.omapzoom.org/repo/x-loader.git
  cd x-loader
  git checkout -b omap4_dev origin/omap4_dev
  make omap4430panda_config
  make ift
  cp -a MLO ~/panda_work/mydroid/device/ti/panda/xloader.bin
Notes: 吸出xīchū,抽出chōuchū

## Slide 61: Download & Build u-boot
Second Boot Loader for Pandaboard
  cd ~/panda_work
  git clone git://git.omapzoom.org/repo/u-boot.git
  cd u-boot
  git checkout -b omap4_dev origin/omap4_dev
  wget http://android-development-environment.googlecode.com/files/0001-change-bootarges.patch
  git apply 0001-change-bootarges.patch
  make omap4430panda_config
  make
  cp -a u-boot.bin ~/panda_work/mydroid/device/ti/panda/bootloader.bin
Notes: 吸出xīchū,抽出chōuchū

## Slide 62: Download & Build kernel
Kernel for Pandaboard
  cd ~/panda_work
  git clone https://android.googlesource.com/kernel/omap.git kernel
  cd kernel
  git checkout -b android-omap-panda-3.0 origin/android-omap-panda-3.0
  make panda_defconfig
  make
  cp -a arch/arm/boot/zImage ~/panda_work/mydroid/device/ti/panda/kernel
Notes: 吸出xīchū,抽出chōuchū

## Slide 63: Build Android
Build Android
  cd ~/panda_work/mydroid
  source build/envsetup.sh
  lunch aosp_panda-userdebug
  make
Notes: 吸出xīchū,抽出chōuchū

## Slide 64: Setup SD Card
Make Partition for Android on SD Card
  boot
  system
  cache
  userdata
  media
  wget http://www.noritsuna.com/download/mksdcard_pandaboard.sh
  chmod a+x mksdcard_pandaboard.sh
  LANG=C sudo ./mksdcard_pandaboard.sh /dev/sdX ~/panda_work/mydroid
Notes: 吸出xīchū,抽出chōuchū

## Slide 65
Extra Stage

## Slide 66
How to Use JTAG-ICE

## Slide 67: Debugging by ICE(In Circuit Emulator)
Full ICE
  This has CPU&CPU Debugging Func.
  When you use it, you change Real CPU to This CPU.
JTAG ICE
  Real CPU has Debugging Func.
  JTAG is Control Pin for CPU Debugging Func,

## Slide 68: Why Need?
Soft Level Debugger can debug
their managed apps only.
  Ex. Kernel Panic: Console Log Only
  Ex. DDMS: Android Framework
  managed Linux Lib

## Slide 69
How to Setup JTAG-ICE

## Slide 70: Flyswatter2 Pandaboard
One of Cheapest JTAG-ICE.
  Today, getting popular under $300USD.
    Old one is Over $3000USD

## Slide 71: Setup udev
Register your board to udev.
  Add the following line to ‘/etc/udev/rules.d/51-android.rules’
  Restart ‘udev’ service
  # usbboot protocol on panda (PandaBoard)
  SUBSYSTEM=="usb", ATTR{idVendor}=="0451", ATTR{idProduct}=="d00f", MODE="0666", OWNER="<username>"
  # usbboot protocol on panda (PandaBoard ES)
  SUBSYSTEM=="usb", ATTR{idVendor}=="0451", ATTR{idProduct}=="d010", MODE="0666", OWNER="<username>"
  SUBSYSTEM=="usb", ATTR{idVendor}=="0451", ATTR{idProduct}=="d022", MODE="0666", OWNER="<username>"

## Slide 72: Add Debug Information to Source Code
What’s Debug Information?
  Executed File(Compiled File) is machine code.
  Human can NOT read it…
  Ex. gcc (DWARF)
    -g(n)
      Debug Option. n=Debug Level
    –O0
      Optimized Option & Level. 0=non-optimized. Always use “3”.
  I/DEBUG ( 3037): pid: 3233, tid: 3234 >>> /system/bin/netd <<<
  I/DEBUG ( 3037): signal 11 (SIGSEGV), fault addr deadbaad
  I/DEBUG ( 3037): r0 00001728 r1 100ffd7c r2 00000027 r3 00000000
  I/DEBUG ( 3037): r4 afd42328 r5 00000000 r6 00000000 r7 00011000
  I/DEBUG ( 3037): r8 00100000 r9 aef01cad 10 10000000 fp 40008008
  I/DEBUG ( 3037): ip ffffffff sp 100ffd68 lr deadbaad pc afd11ca4 cpsr 40000030
  I/DEBUG ( 3037): d0 3d454d414e564544 d1 6164732f7665642f

## Slide 73: Change KGDB Config
Turn On Kernel Config
  Kernel hacking
    Compile the kernel with debug info
    KGDB： kernel degugger
      KGDB: user kgdb over the serial console (NEW)
  cd ~/panda_work/kernel
  make menuconfig
  make
Notes: 吸出xīchū,抽出chōuchū

## Slide 74: Change KGDB Config

## Slide 75: Change u-boot
Need Boot Option for KGDB
  “kgdboc=ttyO2,115200” in “bootargs” section
  wget http://www.noritsuna.com/download/0001-change-bootarges.patch
  git apply 0001-change-bootarges.patch
  make
  cp -a u-boot.bin ~/panda_work/mydroid/device/ti/panda/bootloader.bin
Notes: 吸出xīchū,抽出chōuchū

## Slide 76: Old u-boot
Different Point
  cd ~/panda_work
  git clone git://git.omapzoom.org/repo/u-boot.git
  cd u-boot
  git checkout -b omap4_dev origin/omap4_dev
  wget http://android-development-environment.googlecode.com/files/0001-change-bootarges.patch
  git apply 0001-change-bootarges.patch
  make omap4430panda_config
  make
  cp -a u-boot.bin ~/panda_work/mydroid/device/ti/panda/bootloader.bin
Notes: 吸出xīchū,抽出chōuchū

## Slide 77: Setup Debugging Software
Why Need?
  How do you debug it???
If your code has DWARF(Debug Info), you can use “objdump” command.
  arm-eabi-objdump -S -C libc.so |less
    -S Show de-assembler source code
    -C Show C/C++ function name of source code
    bionic/libc/unistd/abort.c
  #00 pc 00011ca4 /system/lib/libc.so
  11ca4: f005 ff25 bl 11c40 <abort>

## Slide 78: Setup Debugging Software

## Slide 79: Setup FTDI Driver (Serial)
  cd ~/panda_work
  wget http://www.intra2net.com/en/developer/libftdi/download/libftdi-0.19.tar.gz
  tar zxfv libftdi-0.19.tar.gz
  cd ~/panda_work/libftdi-0.19/src
  sudo cp ftdi.h /usr/include
  cd /usr/local/include
  sudo ln -s /usr/include/ftdi.h ftdi.h
  cd ~/panda_work/libftdi-0.19
  ./configure
  make
  sudo make install
  cd /usr/lib
  sudo ln -s /usr/local/lib/libftdi.a libftdi.a
  sudo ln -s /usr/local/lib/libftdi.la libftdi.la
  sudo ln -s /usr/local/lib/libftdi.so.1.19.0 libftdi.so.1.19.0
  sudo ln -s /usr/local/lib/libftdi.so.1.19.0 libftdi.so
  sudo ln -s /usr/local/lib/libftdi.so.1.19.0 libftdi.so.1
Notes: 吸出xīchū,抽出chōuchū

## Slide 80: Setup OpenODC(On-Chip Debugging)
This Debugger is Software for JTAG Debugger.
  Hardware JTAG Debugger get “RAW Data” only.
  cd ~/panda_work
  wget http://downloads.sourceforge.net/project/openocd.berlios/openocd-0.5.0.tar.gz
  tar zxfv openocd-0.5.0.tar.gz
  cd ~/panda_work/openocd-0.5.0
  wget http://www.tincantools.com/w/images/5/5d/Tincantools-openocd-b0.12.patch
  patch -p1 -i Tincantools-openocd-b0.12.patch
  sudo ./configure --disable-werror --enable-ft2232_libftdi
  sudo make
  sudo make install
Notes: 吸出xīchū,抽出chōuchū

## Slide 81: Prepare JTAG Tools
JTAG Commands
  cd ~/panda_work
  mkdir openocd-bin
  cd ~/panda_work/openocd-0.5.0/tcl
  cp -r * ~/panda_work/openocd-bin
  cd ~/panda_work/openocd-0.5.0/src
  cp openocd ~/panda_work/openocd-bin
  export PATH=$PATH:~/panda_work/openocd-bin
Notes: 吸出xīchū,抽出chōuchū

## Slide 82: Connect Cables

## Slide 83: Connect JTAG Debugger
This tool uses telnet command.
  cd ~/panda_work/openocd-bin
  sudo ./openocd -f interface/flyswatter2.cfg -f board/ti_pandaboard.cfg
  telnet localhost 4444
Notes: 吸出xīchū,抽出chōuchū

## Slide 84: JTAG Commands
reset, halt, resume
  Use for Break Point
reg
  reg
    Show register
  reg [entry]
    Show entry register
  reg [entry] [value]
    Set value to entry register

## Slide 85: Setup DDD(Data Display Debugger)
GUI Debugger
  sudo apt-get install ddd

## Slide 86: How to Use Debugger
Start OpenOCD
Connect Console, And exec “halt”
Start DDD
  sudo ./openocd -f interface/flyswatter2.cfg -f board/ti_pandaboard.cfg
  telnet localhost 4444
  > halt
  $ ddd --debugger arm-eabi-gdb
  GDB Console
  (gdb) file vmlinux
  (gdb) target remote localhost:3333

## Slide 87: Ex. Break Point
Stop
  "resume" command on telnet
Do exec
  "c" command on DDD GDB Console

## Slide 88
Appendix: How to Build Others
Notes: 共通gòngtōng
安装ānzhuāng

## Slide 89
AllWinner - A31 (Cortex-A7 Quad)

## Slide 90: AllWinner - A31 (Cortex-A7 Quad)
Target
  Tablet
    Onda V973 (v2)
      http://www.onda.cn/Tablet/ProductInfo.aspx?ProductId=250
OS
  Android
    UnOfficial CyanogenMod
      http://www.slatedroid.com/topic/77481-rom-aokp-42-for-allwinner-a31-devices-sdk-32-2013-07-27-update/

## Slide 91: AllWinner - A31 (Cortex-A7 Quad)
Notes: 取消qǔxiāo
[到手]dàoshǒu

## Slide 92
RockChip - RK3188 (Cortex-A9 Quad)

## Slide 93: RockChip - RK3188 (Cortex-A9 Quad)
Target
  Mini PC
    MK802IV
      http://www.cloudsto.com/android-mini-pc-s/rikomagic-quad-core-mk802iv-8gb-flash-bluetooth-dhl-express-shipping-detail.html
OS
  Official Kernel
    (But No Android&Ubuntu)
    http://www.rikomagic.co.uk/forum/viewtopic.php?f=6&t=4696

## Slide 94: RockChip - RK3188 (Cortex-A9 Quad)
Setup Process
  Put Serial Connector on board.
  Customize kernel
  Make boot-image
  Write new boot-image
Notes: 安装ānzhuāng
连接liánjiē
定制dìngzhì,改造gǎizào,改组gǎizǔ
注上zhùshàng

## Slide 95: Put Serial Connector on board
This connect is TTL level Serial.
Notes: 连接liánjiē
连接器liánjiēqì
[焊料]hànliào

## Slide 96: Customize kernel
Almost Official Kernel doesn’t work…
  naobsd released customized kernel.
    https://github.com/linux-rockchip/rockchip-3.0/tree/reference/mk802iv-ap6210
Build this kernel
  git clone https://github.com/linux-rockchip/rockchip-3.0.git
  cd rockchip-3.0
  git checkout wip/rockchip-3.0-mk802iv-ap6210
  make rk3188_mk802iv_ap6210_defconfig
  make CROSS_COMPILE=../prebuilts/gcc/linux-x86/arm/arm-eabi-4.6/bin/arm-eabi- kernel.img
  make CROSS_COMPILE=../prebuilts/gcc/linux-x86/arm/arm-eabi-4.6/bin/arm-eabi- zImage

## Slide 97: Make boot-image 1/4
Get Original Firmware
  http://www.rikomagic.co.uk/support.html
    This firmware has firmware image file & writing tool.
Unpack Firmware
  https://github.com/naobsd/rkutils
  wget https://raw.github.com/naobsd/rkutils/master/rkunpack.c
  gcc -o rkunpack rkunpack.c
  ./rkunpack IV_AP6210_20130905_1080P.img
Notes: 原物yuánwù
[固件]gùjiàn
打開
包裝

## Slide 98: Make boot-image 2/4
Unpack boot-image
  https://github.com/naobsd/cm_system_core/tree/ics/mkbootimg
  wget https://raw.github.com/naobsd/cm_system_core/ics/mkbootimg/unpackbootimg.c
  wget https://raw.github.com/naobsd/cm_system_core/ics/mkbootimg/bootimg.h
  gcc -o unpackbootimg unpackbootimg.c –lcrypto
  ./unpackbootimg -i boot.img
    ※boot.img-base, boot.img-cmdline, boot.img-pagesize, boot.img-ramdisk.gz, boot.img-zImage
Notes: 打開

## Slide 99: Make boot-image 3/4
Unpack ramdisk
  boot.img-ramdisk.gz
  If your new kernel has new functions, please modify ramdisk files.
    Ex. .ko file, new init file, etc.
  mkdir ramdisk
  cd ramdisk
  gunzip -c ../boot.img-ramdisk.gz | cpio –I
Notes: 打開

## Slide 100: Make boot-image 4/4
Re-pack ramdisk & boot-image
  https://github.com/naobsd/cm_system_core/tree/ics/mkbootimg
  find . | cpio -o -H newc | gzip ../newramdisk.cpio.gz
  cd ../
  wget https://raw.github.com/naobsd/cm_system_core/ics/mkbootimg/mkbootimg.c
  gcc -o mkbootimg mkbootimg.c –lcrypto
  ./mkbootimg --kernel zImage --ramdisk newramdisk.cpio.gz -o mynewboot.img
    ※zImage is your new kernel
Notes: 包裝

## Slide 101: Write new boot-image 1/4
Setup driver for Windows
  Execute “DriverInstall.exe”
Update firmware to new firmware
  Execute “RKBatchTool.exe”
Notes: 驅動器
[更新]gēngxīn
执行[zhíxíng]

## Slide 102: Write new boot-image 2/4
Use RockChip writing tool
  Download writing tool
    http://www.filecrop.com/RKAndroidTool-1.37.html
  Execute “RKAndroidTool.exe”
    Default Boot Address is “0x00008000”
Notes: 地址dìzhǐ

## Slide 103: Write new boot-image 3/4
  Execute “RKAndroidTool.exe”
    Change Boot Address “0x0000C000”

## Slide 104: Write new boot-image 4/4

## Slide 105
MediaTek - MT6589 (Cortex-A7 Quad)

## Slide 106: MediaTek - MT6589 (Cortex-A7 Quad)
Target
  Smart Phone
    Acer Liquid E2
      http://www.acer.com.tw/ac/zh/TW/content/model/HM.HC5TA.001
OS
  Official Kernel & Android
    (But patch only)
    http://us.acer.com/ac/en/US/content/drivers
Notes: 修補
修改[xiūgǎi]

## Slide 107: MediaTek - MT6589 (Cortex-A7 Quad)
Setup Process
  Get kernel source code & patch for Android-4.2.1
  Merge AOSP & this patch
  Build kernel
  Copy drivers for Android
  Modify Android source code
  Build Android image
  Write Android image to your phone
Notes: [合并]hébìng
修補
修改[xiūgǎi]

## Slide 108: Get kernel source code & patch for Android-4.2.1
Download Acer's source code
  wget
    http://global-download.acer.com/GDFiles/Document/App.%20Guide/App.%20Guide_Acer_1.0_A42J_A.zip?acerid=635013347354221361&Step1=Smartphone&Step2=Liquid%20E2&Step3=V370&OS=---&LC=en&BC=Acer&SC=EMEA_8
      Acer_AV061_V370_1.007.00_WW_GEN1_opensource.tar.gz
    http://global-download.acer.com/GDFiles/Document/App.%20Guide/App.%20Guide_Acer_1.0_A_A.zip?acerid=635139433116342519&Step1=SMARTPHONE&Step2=LIQUID%20E2&Step3=V370&OS=ALL&LC=en&BC=ACER&SC=PA_6
      C11_opensource_20130903.tar
Notes: [下载]xiàzǎi
打開
现xiàn
修補
修改[xiūgǎi]

## Slide 109: Marge AOSP & this patch
Download source tree of android JB from AOSP
Marge source
  Over-write external,system,bootable,bionic dirs
    from Acer_AV061_V370_1.007.00_WW_GEN1_opensource.tar.gz
  Add mediatek, kernel dirs
    from C11_opensource_20130903.tar
  repo init -u https://android.googlesource.com/platform/manifest -b android-4.2.1_r1.2
  repo sync
Notes: [合并]hébìng
[复制]fùzhì
重寫
修補
修改[xiūgǎi]

## Slide 110: Build kernel
Build kernel for MT6589
  export PATH=[your android dir for MT6589]/prebuilts/gcc/linux-x86/arm/arm-linux-androideabi-4.6/bin:$PATH
  cd [your android dir for MT6589]/kernel
  TARGET_PRODUCT=simcom89_wet_jb2 MTK_ROOT_CUSTOM=../mediatek/custom/ make
Notes: 建立

## Slide 111: Copy drivers for Android
Some source code & driver aren’t released.
  Copy them from update image
    wget http://global-download.acer.com/GDFiles/OS/OS/OS_Acer_Acer.AV061.V370.1.023.00.WW.GEN1_A42J_A.zip?acerid=635158485778733078&Step1=SMARTPHONE&Step2=LIQUID%20E2&Step3=V370&OS=ALL&LC=en&BC=ACER&SC=PA_6
      OS_Acer_Acer.AV061.V370.1.023.00.WW.GEN1_A42J_A.zip
    Copy system/vendor, system/lib dirs to Android device dir

## Slide 112: Modify Android source code 1/2
Delete libcustom_prop
  ./external/webkit/Android.mk
  ./external/webkit/Source/WebCore/loader/FrameLoader.cpp
LOCAL_C_INCLUDES += mediatek/frameworks/base/custom/inc
LOCAL_STATIC_LIBRARIES += libcustom_prop
#include "custom_prop.h“
※And “m_customXWapProfile” functions
Notes: 删掉shāndiào,删除shānchú

## Slide 113: Modify Android source code 2/2
Delete libcustom_prop
  ./external/webkit/Source/WebCore/platform/network/android/SocketStreamHandle.h
  ./external/webkit/Source/WebCore/css/CSSComputedStyleDeclaration.cpp
  ./external/webkit/Source/WebCore/css/CSSParser.cpp
  ./external/webkit/Source/WebCore/loader/appcache/ApplicationCacheHost.cpp
  ./external/webkit/Source/WebCore/websockets/WebSocket.cpp
  ./external/webkit/Source/WebCore/xml/XMLHttpRequest.cpp
  ./external/webkit/Source/WebCore/websockets/WebSocketHandshake.cpp
  ./external/webkit/Source/WebKit/android/WebCoreSupport/WebViewClientError.cpp
  ./external/webkit/Source/WebCore/websockets/WebSocketChannel.cpp
  ./external/webkit/Source/WebKit/android/WebCoreSupport/SocketStreamHandleAndroid.cpp
  ./external/webkit/Source/WebKit/android/WebCoreSupport/SocketStreamHost.cpp
#include <cutils/xlog.h>
※And “XLOG” functions
Notes: 删掉shāndiào,删除shānchú

## Slide 114: Build Android image
  . build/envsetup.sh
  choosecombo
  Build type choices are:
  1. release
  2. debug
  Which would you like? [1] 1
  Which product would you like? [full] full
  Variant choices are:
  1. user
  2. userdebug
  3. eng
  Which would you like? [eng] 3
  make dist
  out/dist/full-target_files-eng.[your user name].zip
Notes: 建立

## Slide 115: Write Android image to your phone
adb push out/dist/full-target_files-eng.[your user name].zip /sdcard/
Turn off your phone
Volume Up & Power
Wipe data/factory reset
Install zip from sdcard
Choose zip from sdcard
full-target_files-eng.[your user name].zip
+++++Go Back+++++
Reboot system now
Notes: 推tuī
關機
删掉shāndiào,删除shānchú
[安装]ānzhuāng
[取向]qǔxiàng
[重新启动]chóngxīn qǐdòng

## Slide 116
Freescale - i.MX6Q (Cortex-A9 Quad)

## Slide 117: Freescale - i.MX6Q (Cortex-A9 Quad)
Target
  EVB
    i.MX6Q SABRA Lite
      http://www.cloudsto.com/android-mini-pc-s/rikomagic-quad-core-mk802iv-8gb-flash-bluetooth-dhl-express-shipping-detail.html
OS
  Official Kernel & Android
    With Setup Manual
    http://www.freescale.com/webapp/search/Serp.jsp?QueryText=android&assetIdResult=&attempt=0&lastQueryText=android&isFromFlex=false&getResult=false&assetLockedForNavigation=false&pageNum=2&iteration=2&fsrch=1&isComparison=false&showAllCategories=false&sessionChecker=cTqD1ZGIFEqGCbd9lV29IKvJ.ebiz_ms2&getTree=false&fromTrng=false&fromPSP=false&getFilter=false&assetLocked=false&fromCust=false&showCustomCollateral=false&pageSize=25&RELEVANCE=true&SelectedAsset=Downloads&fromWebPages=false&fromASP=false&fromMobile=false&isAdvanceSearch=false&isTree=false&fromDAP=false&isResult=false

## Slide 118: Freescale - i.MX6Q (Cortex-A9 Quad)
Setup Process
  Download Source Code from Official Site
  Patch to Android Source Code
  Modify Android Source Code for SD Card
  Fix 32bit files
  Build Source Codes
    Android
    u-boot
    boot-image
  Setup SD Card
Notes: 改修ɡǎixiū

## Slide 119: Download Source Code from Official Site
Download Android
Download Kernel
  repo init -u https://android.googlesource.com/platform/manifest -b android-4.2.2_r1
  repo sync
  git clone git://git.freescale.com/imx/linux-2.6-imx.git kernel_imx
  cd kernel_imx
  git checkout jb4.2.2_1.1.0-ga
Notes: 下载xiàzài

## Slide 120: Download Source Code from Official Site
Download bootloader
Download Patch
  https://www.freescale.com/webapp/Download?colCode=IMX6_JB422_110_ANDRD_SRC_BSP&appType=license&location=null&fpsp=1&WT_TYPE=Board%20Support%20Packages&WT_VENDOR=FREESCALE&WT_FILE_FORMAT=gz&WT_ASSET=Downloads&sr=38&Parent_nodeId=from%20search&Parent_pageType=from%20search
    android_jb4.2.2_1.1.0-ga.tar.gz
  cd ../bootable
  cd bootloader
  git clone https://github.com/ldnunes/uboot-imx.git uboot-imx
  cd uboot-imx
  git checkout jb4.2.2_1.1.0-ga
Notes: 下载xiàzài
修補
修改[xiūgǎi]

## Slide 121: Patch to Android Source Code
Patch
  cd [your Android dir]
  tar zxfv android_jb4.2.2_1.1.0-ga.tar.gz
  tar zxfv android_jb4.2.2_1.1.0-ga_source.tar.gz
  cd android_jb4.2.2_1.1.0-ga_source/code/
  tar zxfv jb4.2.2_1.1.0-ga.tar.gz
  cd ../../
  source android_jb4.2.2_1.1.0-ga_source/code/jb4.2.2_1.1.0-ga/and_patch.sh
  c_patch android_jb4.2.2_1.1.0-ga_source/code/jb4.2.2_1.1.0-ga imx_jb4.2.2_1.1.0-ga
Notes: 修補
修改[xiūgǎi]

## Slide 122: Modify Android Source Code for SD Card
device/fsl/imx6/etc/fstab.freescale
  Create New File(Please delete it, if exist.)
  /dev/block/mmcblk1p5 /system ext4 ro wait
  /dev/block/mmcblk1p4 /data ext4 nosuid,nodev,nodiratime,noatime,nomblk_io_submit,noauto_da_alloc,errors=panic wait
  /dev/block/mmcblk1p6 /cache ext4 nosuid,nodev,nomblk_io_submit wait
  /dev/block/mmcblk1p7 /device ext4 ro,nosuid,nodev wait

## Slide 123: Modify Android Source Code for SD Card
device/fsl/sabresd_6dq/recovery.fstab
  Create New File(Please delete it, if exist.)
  /boot emmc /dev/block/mmcblk1p1
  /recovery emmc /dev/block/mmcblk1p2
  /system ext4 /dev/block/mmcblk1p5
  /cache ext4 /dev/block/mmcblk1p6
  /data ext4 /dev/block/mmcblk1p4 reserved=32768
  /misc emmc /dev/block/mmcblk1p8
  /sdcard vfat /dev/block/mmcblk1p1

## Slide 124: Modify Android Source Code for SD Card
device/fsl/sabresd_6dq/vold.fstab b/device/fsl/sabresd_6dq/vold.fstab
  Modify it:
  @@ -26,7 +26,7 @@
  #used for all usb host
  dev_mount udisk /mnt/udisk auto /devices/platform/fsl-ehci
  #mount SDHC4 SD card /mnt/sdcard as primary storage for MX6Q SABER_LITE RevC
  -dev_mount extsd /mnt/extsd auto /devices/platform/sdhci-esdhc-imx.2/mmc_host/mmc1
  +dev_mount extsd /mnt/extsd auto /devices/platform/sdhci-esdhc-imx.1/mmc_host/mmc2
  #mount SDHC3 TF card to /mnt/extsd as external storage forMX6Q SABER_LITE RevC
  #dev_mount sdcard /mnt/sdcard 4 /devices/platform/sdhci-esdhc-imx.3/mmc_host/mmc0

## Slide 125: Fix 32bit files 1/4
Setup files
  sudo apt-get install
    uuid uuid-dev zlib1g-dev liblz-dev liblzo2-2 liblzo2-de
Download 32bits files
  wget https://community.freescale.com/servlet/JiveServlet/download/312916-255326/liblzo2-2_2.05-1_i386.deb.zip
  wget https://community.freescale.com/servlet/JiveServlet/download/312916-255325/liblzo2-dev_2.05-1_i386.deb.zip
  wget https://community.freescale.com/servlet/JiveServlet/download/312916-255364/mtd-utils.tgz
  wget https://community.freescale.com/servlet/JiveServlet/download/312916-258740/uuid-dev_2.20.1-1ubuntu3_i386.deb.zip

## Slide 126: Fix 32bit files 2/4
Setup 32bits files
  Install liblzo2 & uuid
  unzip liblzo2-2_2.05-1_i386.deb.zip
  unzip liblzo2-dev_2.05-1_i386.deb.zip
  unzip uuid-dev_2.20.1-1ubuntu3_i386.deb.zip
  sudo mkdir /usr/lib/liblzo2_i386
  sudo mkdir /usr/lib/uuid-dev_i386
  sudo dpkg -x liblzo2-dev_2.05-1_i386.deb /usr/lib/liblzo2_i386/
  sudo dpkg -x liblzo2-2_2.05-1_i386.deb /usr/lib/liblzo2_i386/
  sudo dpkg -x uuid-dev_2.20.1-1ubuntu3_i386.deb /usr/lib/uuid-dev_i386/

## Slide 127: Fix 32bit files 3/4
Setup 32bits files
  Re-link liblzo2 & uuid
  sudo rm liblzo2.a
  sudo rm liblzo2.so
  sudo rm liblzo2.so.2
  sudo ln -s liblzo2_i386/usr/lib/liblzo2.a liblzo2.a
  sudo ln -s liblzo2_i386/usr/lib/liblzo2.so.2.0.0 liblzo2.so
  sudo ln -s liblzo2_i386/usr/lib/liblzo2.so.2.0.0 liblzo2.so.2
  sudo ln -s uuid-dev_i386/usr/lib/i386-linux-gnu/libuuid.a libuuid.a
  sudo ln -s uuid-dev_i386/usr/lib/i386-linux-gnu/libuuid.so libuuid.so

## Slide 128: Fix 32bit files 4/4
Modify
  external/mtd-utils/mkfs.ubifs/Android.mk
  LOCAL_LDFLAGS +=-L /usr/lib/
  LOCAL_C_INCLUDES +=/usr/lib/uuid-dev/usr/include/
  LOCAL_C_INCLUDES +=/usr/lib/liblzo2_i386/usr/include

## Slide 129: Build Source Codes 1/3
Build Android
  cd [your Android dir]
  source build/envsetup.sh
  lunch sabresd_6dq-user
  make

## Slide 130: Build Source Codes 2/3
Build u-boot
  cd [your Android dir]/bootable/bootloader/uboot-imx
  export ARCH=arm
  export CROSS_COMPILE=[your Android dir]/prebuilts/gcc/linux-x86/arm/arm-eabi-4.6/bin/arm-eabi-
  make distclean
  make mx6q_sabresd_android_config
  make

## Slide 131: Build Source Codes 3/3
Build kernel
Build boot-image
  export ARCH=arm
  export CROSS_COMPILE=[your Android dir]/prebuilts/gcc/linux-x86/arm/arm-eabi-4.6/bin/arm-eabi-
  make imx6_android_defconfig
  make uImage
  cd [your Android dir]
  source build/envsetup.sh
  lunch sabresd_6dq-user
  make bootimage

## Slide 132: Setup SD Card
If you want to boot from SD Card, you have to make a special sector for this board.
  This script can make the special sector.
  cd [your Android dir]
  cp ./out/target/product/sabresd_6dq/*.img .
  chmod +x ./device/fsl/common/tools/fsl-sdcard-partition.sh
  sudo ./device/fsl/common/tools/fsl-sdcard-partition.sh /dev/sdX
  ※X is your SD Card device name

## Slide 133
TI - OMAP5432 (Cortex-A15 Dual)

## Slide 134: TI - OMAP5432 (Cortex-A15 Dual)
Target
  EVB
    OMAP5432-EVM
      http://www.ti.com/tool/omap5432-evm?DCMP=omap-5432evm-130521&HQS=omap-5432evm-b-sw
OS
  Official Kernel & Android
    With Build Manual&Data Sheet
    http://www.ti.com/tool/omap5432-evm-eval-sw
    http://omapedia.org/wiki/Panda5AJ.1.5_Release_Notes

## Slide 135: TI - OMAP5432 (Cortex-A15 Dual)
Setup Process
  Download Android Source Code
  Build Android Source Code
  Download kernel Source Code
  Build kernel Source Code
  Download u-boot Source Code
  Build u-boot Source Code
  Build fastboot image
  Write fastboot images to eMMC

## Slide 136: Download Android Source Code
Download Android
  cd [your Panda5 dir]
  mkdir -p mydroid
  cd mydroid
  export MYDROID=`pwd`
  repo init -u git://git.omapzoom.org/platform/omapmanifest.git -b 5AJ.x -m RLS_panda5AJ.1.5.xml
  repo sync

## Slide 137: Build Android Source Code
Build Android system
  . build/envsetup.sh
  lunch 25
  make clean
  make

## Slide 138: Download kernel Source Code
Download kernel
  cd [your Panda5 dir]
  mkdir kernel
  git clone git://git.omapzoom.org/kernel/omap.git kernel/android-3.4
  cd kernel/android-3.4
  git checkout 499e8d5a5aa8a271bf9c4ae404ad234b7fb22b9f

## Slide 139: Build kernel Source Code 1/2
Build kernel
  export PATH=$PATH:${MYDROID}/prebuilts/gcc/linux-x86/arm/arm-eabi-4.6/bin/
  export CROSS_COMPILE=${MYDROID}/prebuilts/gcc/linux-x86/arm/arm-eabi-4.6/bin/arm-eabi-
  cd [your Panda5 dir]/kernel/android-3.4
  make ARCH=arm mrproper
  make ARCH=arm android_omap_defconfig
  make ARCH=arm uImage modules

## Slide 140: Build kernel Source Code 2/2
Build Wi-Fi Driver
  export KERNEL_DIR=[your Panda5 dir]/kernel/android-3.4
  export KLIB=${KERNEL_DIR}
  export KLIB_BUILD=${KERNEL_DIR}
  cd ${MYDROID}/hardware/ti/wlan/mac80211/compat_wl18xx/
  make ARCH=arm

## Slide 141: Download u-boot Source Code
Download u-boot
  cd [your Panda5 dir]
  git clone git://git.omapzoom.org/repo/omapboot.git usbboot
  cd usbboot
  git checkout 33af7cb409b603cf7988306ab2ea70f052a9a02b

## Slide 142: Build u-boot Source Code
Build u-boot
  cd [your Panda5 dir]/usbboot
  make MACH=omap5 BOARD=omap5uevm clean
  make MACH=omap5 BOARD=omap5uevm

## Slide 143: Build fastboot image 1/2
Copy kernel to OTA image dir
Copy Wi-Fi Drivers to OTA image dir
  cd $MYDROID
  cp -v [your Panda5 dir]/kernel/android-3.4/arch/arm/boot/zImage device/ti/panda5/kernel
  cd $MYDROID/out/target/product/panda5
  mkdir -p system/lib/modules; cd system/lib/modules
  cp -fp ${MYDROID}/hardware/ti/wlan/mac80211/compat_wl18xx/compat/compat.ko .
  cp -fp ${MYDROID}/hardware/ti/wlan/mac80211/compat_wl18xx/net/wireless/cfg80211.ko .
  cp -fp ${MYDROID}/hardware/ti/wlan/mac80211/compat_wl18xx/net/mac80211/mac80211.ko .
  cp -fp ${MYDROID}/hardware/ti/wlan/mac80211/compat_wl18xx/drivers/net/wireless/ti/wl12xx/wl12xx.ko .
  cp -fp ${MYDROID}/hardware/ti/wlan/mac80211/compat_wl18xx/drivers/net/wireless/ti/wl18xx/wl18xx.ko .
  cp -fp ${MYDROID}/hardware/ti/wlan/mac80211/compat_wl18xx/drivers/net/wireless/ti/wlcore/wlcore*.ko .
Notes: 拷贝[kǎobèi]

## Slide 144: Build fastboot image 2/2
ReBuild Android System
  cd $MYDROID
  . build/envsetup.sh
  lunch 25
  rm out/target/product/panda5/*img
  rm out/target/product/panda5/obj/PACKAGING/systemimage_intermediates/system.img
  make

## Slide 145: Write fastboot images to eMMC 1/6
Copy fastboot images to working dir
  cd [your Panda5 dir]
  mkdir emmc_files
  cp -v ${MYDROID}/out/target/product/panda5/*img emmc_files
  cp -v ${MYDROID}/device/ti/omap5sevm/boot/fastboot.sh emmc_files
  cp -v ${MYDROID}/out/host/linux-x86/bin/{simg2img,make_ext4fs,mkbootimg,fastboot,adb} emmc_files
  cp -v [your Panda5 dir]/kernel/android-3.4/arch/arm/boot/zImage emmc_files/kernel
  cp -v [your Panda5 dir]/usbboot/out/omap5uevm/omap5uevm_GP_ES2.0_MLO emmc_files
  cp -v [your Panda5 dir]/usbboot/out/omap5uevm/usbboot emmc_files

## Slide 146: Write fastboot images to eMMC 2/6
Register your board to udev.
  Add the following line to ‘/etc/udev/rules.d/51-android.rules’
  Restart ‘udev’ service
  SUBSYSTEM=="usb", ATTRS{idVendor}=="0451", ATTRS{idProduct}=="d011", MODE="0666"
Notes: 补记bǔjì

## Slide 147: Write fastboot images to eMMC 3/6
Connect 2 Cables to PC
  Serial Connecter
    This connecter is MicroUSB.
  USB Connecter for ADB
    This port is USB3.0 connecter.
    Connect USB2.0 Cable.

## Slide 148: Write fastboot images to eMMC 4/6
Run fastboot program on your PC
  cd [your Panda5 dir]/emmc_files
  sudo ./usbboot –f
  “waiting for device..”

## Slide 149: Write fastboot images to eMMC 5/6
Boot-up your board from eMMC
  Change boot-up dip switch to SW1-4=OFF
Notes: 转换zhuǎnhuàn

## Slide 150: Write fastboot images to eMMC 6/6
Write All Images to eMMC
  sudo ./fastboot.sh

## Slide 151
Samsung - Exynos5 (Cortex-A15 Quad and Cortex-A7 Quad)

## Slide 152: Samsung - Exynos5 (Cortex-A15 Quad and Cortex-A7 Quad)
Target
  EVB
    ODROID-XU
      http://www.hardkernel.com/renewal_2011/products/prdt_info.php?g_code=G137510300620
OS
  Official Kernel & Android
    With Build Manual&Data Sheet
    http://odroid.com/dokuwiki/doku.php?id=en:odroid-xu

## Slide 153: Samsung - Exynos5 (Cortex-A15 Quad and Cortex-A7 Quad)
OS
  Official Kernel & Android
    With Build Manual&Block Fig
    http://odroid.com/dokuwiki/doku.php?id=en:odroid-xu
Notes: 拒绝jùjué

## Slide 154: Samsung - Exynos5 (Cortex-A15 Quad and Cortex-A7 Quad)
Setup Process
  Build u-boot
  Build kernel
  Build Android
  Setup eMMC
  Write fastboot images to eMMC

## Slide 155: Build u-boot 1/2
Setup Toolchains
Setup Paths
  wget http://dn.odroid.com/ODROID-XU/compiler/arm-eabi-4.4.3.tar.gz
  mkdir [your toolchain dir]
  cp arm-eabi-4.4.3.tar.gz [your toolchain dir]
  cd [your toolchain dir]
  tar zxvf arm-eabi-4.4.3.tar.gz
  export PATH=${PATH}:[your toolchain dir]/arm-eabi-4.4.3/bin
  export CROSS_COMPILE=arm-eabi-

## Slide 156: Build u-boot 2/2
Get Source Code with kernel & Android
  http://dn.odroid.com/ODROID-XU/Android_bsp/
    Please get latest Source Code from there.
Build u-boot
  cd uboot
  make distclean
  make smdk5410_config
  make

## Slide 157: Build kernel
Setup Toolschain & Get Source Code
  Same with u-boot. Please see u-boot section.
Build kernel
  cd kernel
  make distclean
  make odroidxu_android_defconfig
  make

## Slide 158: Build Android
Run Build Script
  If you get compile error, please do the following:
    sudo ln -s /usr/lib/i386-linux-gnu/mesa/libGL.so.1 /usr/lib/i386-linux-gnu/libGL.so
  ./build.sh odroidxu platform

## Slide 159: Setup eMMC 1/4
This board doesn’t have boot loader on eMMC.
  Setup boot loader to eMMC from SD Card.
Setup Steps
  Download eMMC setup image for SD Card.
    It’s disk image file for SD Card.
  Write this image to SD Card.
  Boot-up your board from SD Card.
  Setup boot loader to eMMC automatically.

## Slide 160: Setup eMMC 2/4
Download eMMC setup image for SD Card.
    It’s disk image file for SD Card.
Write this image to SD Card.
Boot-up your board from SD Card.
Setup boot loader to eMMC automatically.

## Slide 161: Setup eMMC 3/4
Download eMMC setup image for SD Card
    And unzip.
Write this image to SD Card
    /dev/sdX ‘s X is your SD Card device name.
  wget http://dn.odroid.com/ODROID-XU/Recovery_0.4/emmc_installer.zip
  dd if=./emmc_installer.img of=/dev/sdX

## Slide 162: Setup eMMC 4/4
Boot-up your board from SD Card
  Change boot-up dip switch to SW1=OFF, SW2=ON.
Setup boot loader to eMMC automatically
  Put SD Card on your board.
  Turn on power.
  Wait a minute.
Notes: 转换zhuǎnhuàn
[重启]chóngqǐ

## Slide 163: Write fastboot images to eMMC 1/5
Connect 2 Cables to PC
  Serial Connecter
    This cable is optional parts.
    If you want it, you should buy with board.
  USB Connecter for ADB
    This port is USB3.0 connecter.
    Connect USB2.0 Cable.

## Slide 164: Write fastboot images to eMMC 2/5
Change fastboot mode.
  Show “Press ‘Enter’ or ‘Space’ to stop auto boot”
  Press Enter’ or ‘Space’
Notes: 推tuī

## Slide 165: Write fastboot images to eMMC 3/5
Change fastboot mode.
  Input “fastboot”
Notes: 输入

## Slide 166: Write fastboot images to eMMC 4/5
Register your board to udev.
  Add the following line to ‘/etc/udev/rules.d/51-android.rules’
  Restart ‘udev’ service
  SUBSYSTEM=="usb", ATTRS{idVendor}=="18d1", MODE="0666"

## Slide 167: Write fastboot images to eMMC 5/5
Put your systems to your board.
  Use fastboot
    If your system doesn’t have fastboot, please do:
      sudo apt-get install android-tools-fastboot
  fastboot flash xloader uboot/MLO
  fastboot flash bootloader uboot/u-boot.bin
  fastboot flash kernel kenel/arch/arm/boot/zIamge ※If you write boot partition, it doesn't need.
  fastboot flash boot out/target/product/odroidxu/boot.img
  fastboot flash system android/out/target/product/odroidxu/system.img