## Slide 1: Quick Explanation of Pandaboard
Noritsuna Imamura
noritsuna@siprop.org

## Slide 2: Today’s Topic
  All Things which were Lectured will be Connected!!!
You will Understand why I explain about that.

## Slide 3: Agenda
About Pandaboard
  How to Build Android System
  How to Debug Android System on Pandaboard
Customize Android System
  Add Own API to Android System
  Make Own SDK
How to Use NDK
  Build OpenCV
  Only C/C++ World on Android

## Slide 4
Pandaboard
（Pick Up Important Point）

## Slide 5: What’s Pandaboard?
Target
  EVB
    Pandaboard
      http://www.pandaboard.org/
OS
  Official Kernel & Android
    With Build Manual
    http://source.android.com/source/downloading.html

## Slide 6: How to Use Peripherals?
ADK (Accessory Development Kit)
  http://developer.android.com/tools/adk/index.html
Advantage
  Develop on ADT
  Pin like Arduino
Dis-Advantage
  So Slow…
    9600bps

## Slide 7: How to Use Peripherals?
GPIO(General Purpose Input/Output)
  I2C(Inter-Integrated Circuit)
  SPI(Serial Peripheral Interface)
  UART(Serial)
    Fast: SPI > I2C
    Pin Num: SPI(4Pins) > I2C(3Pins)
    GPIO can use Registers.
Advantage
  Bus Speed
  Connect All Peripheral
Dis-Advantage
  Required Hardware Knowledge
    Like Assembler for Hardware

## Slide 8: Download & Build u-boot
Second Boot Loader for Pandaboard
  cd ~/panda_work
  git clone git://git.omapzoom.org/repo/u-boot.git
  cd u-boot
  git checkout -b omap4_dev origin/omap4_dev
  wget http://android-development-environment.googlecode.com/files/0001-change-bootarges.patch
  git apply 0001-change-bootarges.patch
  make omap4430panda_config
  make
  cp -a u-boot.bin ~/panda_work/mydroid/device/ti/panda/bootloader.bin
Notes: 吸出xīchū,抽出chōuchū

## Slide 9: About boot.scr
Patch Contents
  --- a/include/configs/omap4430panda.h
  +++ b/include/configs/omap4430panda.h
  @@ -147,8 +147,7 @@
  " ip=dhcp"
  #else
  -#define CONFIG_BOOTARGS "console=ttyO2,115200n8 mem=512M" \
  - " init=/init vram=32M omapfb.vram=0:16M androidboot.console=ttyO2"
  +#define CONFIG_BOOTARGS "kgdboc=ttyO2,115200 console=ttyO2,115200n8 mem=1G androidboot.console=ttyO2"

## Slide 10: About boot.scr
Sample of boot.scr: File Name=boot.txt
How to Make
  mkimage -A arm -T script -O linux -C none -a 0 -e 0 -n "boot.scr" -d boot.scr.txt boot.scr
  setenv fdt_high "0xffffffff"
  setenv bootcmd "fatload mmc 0:1 0x80200000 uImage; fatload mmc 0:1 0x81600000 uInitrd; fatload mmc 0:1 0x815f0000 board.dtb; bootm 0x80200000 0x81600000 0x815f0000"
  setenv bootargs "console=ttyO2,115200n8 rootwait ro earlyprintk fixrtc nocompcache vram=48M omapfb.vram=0:24M,1:24M mem=456M@0x80000000 mem=512M@0xA0000000 init=/init androidboot.console=ttyO2 omapfb.mode=dvi:1280x800MR-24@60 consoleblank=0"

## Slide 11: Common Setup 1/2
Setup Build Tools
  sudo apt-get install
    bison build-essential curl flex git-core gnupg gperf libesd0-dev libncurses5-dev libsdl1.2-dev libwxgtk2.8-dev libxml2 libxml2-utils lzop openjdk-6-jdk openjdk-6-jre pngcrush schedtool squashfs-tools xsltproc zip zlib1g-dev
    g++-multilib gcc-multilib lib32ncurses5-dev lib32readline-gplv2-dev lib32z1-dev
Setup Build Tools for ARM
  sudo apt-get install
    uboot-mkimage
Notes: 共通gòngtōng
安装ānzhuāng
工具gōngjù

## Slide 12: But……… TI support until 4.2
2012.06.27 4.1 Jelly Bean
2012.11.13 4.2
2013.07.24 4.3
4.3
  Support OpenGL/ES 3.0
  Support Bluetooth LE
  Support Wi-Fi Location
  Linux: 3.4.0
4.1, 4.2
  Available USB Audio
  Support i18n(Internationalization)
  Support Vibration for Input Device
  Support Miracast
  Support Writing Vertically
  Support RenderScript
  Change Android Market to Google Play
  Linux: 3.1.10

## Slide 13
How to Use JTAG-ICE

## Slide 14: Debugging by ICE(In Circuit Emulator)
Full ICE
  This has CPU&CPU Debugging Func.
  When you use it, you change Real CPU to This CPU.
JTAG ICE
  Real CPU has Debugging Func.
  JTAG is Control Pin for CPU Debugging Func,

## Slide 15: Why Need?
Soft Level Debugger can debug
their managed apps only.
  Ex. Kernel Panic: Console Log Only
  Ex. DDMS: Android Framework
  managed Linux Lib

## Slide 16
How to Setup JTAG-ICE

## Slide 17: Flyswatter2 Pandaboard
One of Cheapest JTAG-ICE.
  Today, getting popular under $300USD.
    Old one is Over $3000USD

## Slide 18: Add Debug Information to Source Code
What’s Debug Information?
  Executed File(Compiled File) is machine code.
  Human can NOT read it…
  Ex. gcc (DWARF)
    -g(n)
      Debug Option. n=Debug Level
    –O0
      Optimized Option & Level. 0=non-optimized. Always use “3”.
  I/DEBUG ( 3037): pid: 3233, tid: 3234 >>> /system/bin/netd <<<
  I/DEBUG ( 3037): signal 11 (SIGSEGV), fault addr deadbaad
  I/DEBUG ( 3037): r0 00001728 r1 100ffd7c r2 00000027 r3 00000000
  I/DEBUG ( 3037): r4 afd42328 r5 00000000 r6 00000000 r7 00011000
  I/DEBUG ( 3037): r8 00100000 r9 aef01cad 10 10000000 fp 40008008
  I/DEBUG ( 3037): ip ffffffff sp 100ffd68 lr deadbaad pc afd11ca4 cpsr 40000030
  I/DEBUG ( 3037): d0 3d454d414e564544 d1 6164732f7665642f

## Slide 19: Change KGDB Config
Turn On Kernel Config
  Kernel hacking
    Compile the kernel with debug info
    KGDB： kernel degugger
      KGDB: user kgdb over the serial console (NEW)
  cd ~/panda_work/kernel
  make menuconfig
  make
Notes: 吸出xīchū,抽出chōuchū

## Slide 20: Change KGDB Config

## Slide 21: Change u-boot
Need Boot Option for KGDB
  “kgdboc=ttyO2,115200” in “bootargs” section
  wget http://www.noritsuna.com/download/0001-change-bootarges.patch
  git apply 0001-change-bootarges.patch
  make
  cp -a u-boot.bin ~/panda_work/mydroid/device/ti/panda/bootloader.bin
Notes: 吸出xīchū,抽出chōuchū

## Slide 22: Setup Debugging Software
Why Need?
  How do you debug it???
If your code has DWARF(Debug Info), you can use “objdump” command.
  arm-eabi-objdump -S -C libc.so |less
    -S Show de-assembler source code
    -C Show C/C++ function name of source code
    bionic/libc/unistd/abort.c
  #00 pc 00011ca4 /system/lib/libc.so
  11ca4: f005 ff25 bl 11c40 <abort>

## Slide 23: Setup Debugging Software

## Slide 24: JTAG Commands
reset, halt, resume
  Use for Break Point
reg
  reg
    Show register
  reg [entry]
    Show entry register
  reg [entry] [value]
    Set value to entry register

## Slide 25: Ex. Break Point
Stop
  "resume" command on telnet
Do exec
  "c" command on DDD GDB Console

## Slide 26: Customize Android System with NDK
Noritsuna Imamura
noritsuna@siprop.org

## Slide 27: About Android
Android Framework has 3 Layer Stack for SmartPhone & Tablet PC.
  Application Framework Layer (Java)
  Library Layer (Linux C/C++)
  Kernel/Driver Layer (Linux Kernel C/ASM)

## Slide 28: Structure of out dir
target/common/obj/
  APPS
    APK
  JAVA_LIBRARIES
    API
  PACKAGING
    Files Nothing...
target/product/flo/
  boot.img
    kernel
    ramdisk.img
    root
  ramdisk-recovery.img
  recovery.img
    recovery
  system.img
    system
  userdata.img
    data
  cache.img
    cache

## Slide 29: What’s Fastboot?
Fastboot is ROM Manager for eMMC.
  eMMC is managed by Address in Low Lovel.
    When you write your Kernel, you MUST point kernel address.
    If you mistake kernel address, your system is broken…
Separated by Address

## Slide 30: About Android Source Code
  packages
    App for Android
  frameworks
    Lib for Android Apps
  system
    Sys Lib for Framework
  docs
    Java Doc for Android
  developers
    Sample, Demos
  build
    Tool for Android Build
  prebuilts
    Toolchain
  sdk
    Android SDK
  ndk
    Native SDK
  pdk
    for 3rd Party SDK
  cts
    Compatibility Test
  tools
    Tools for External

## Slide 31: About Android Source Code
  external
    Linux Lib
  libcore
    Lib for Android
  bionic
    libc for Android
  libnativehelper
    Helper for JNI
  abi
    Application Binary Interface
  dalvik
    Java VM
  art
    Next Generation VM
  device
    Diff for Devices
  hardware
    Drivers
  bootable
    BootLoader

## Slide 32
Customized Android System(ROM)

## Slide 33: What’s Nexus7?
Target
  Tablet
    Nexus7(2013)
      http://www.google.com/nexus/7/
OS
  JCROM
    With Build Manual
    https://sites.google.com/site/jcromproject/

## Slide 34: Customized UI/UX
Modify Android System
  View
  Animation
  SystemUI
  Home
  Widget
  Notification
  Settings
  etc…

## Slide 35: Application Framework Layer
APIs
  App Components
  User Interface
  App Resources
  Animation and Graphics
  Computation
  Media and Camera
  Location and Sensors
  Connectivity
  Text and Input
  Data Storage
  Administration
  Web Apps
  Best Practices

## Slide 36: How to Develop?
ADT
  Standard Android Application
  Only Java on Application Framework Layer
Advantage
  Use All Android Tools
  Many Docs from Google Developer Site & Blogs
APK File(Your Application)
(Java)
Application Framework
Layer (Java)
Library Layer
(C/C++)
Kernel/Driver Layer
(C/ASM)
Call as Java API
Call as JNI(C/C++)
Call as SysCall(C/ASM)
Call Stack

## Slide 37: How to Develop?
NDK w/ADT
  Standard Android Application for C/C++
  Java on Application Framework Layer
  C/C++ on Limited Library Layer
Advantage
  Use Java&C/C++
Dis-Advantage
  Must Use UI Framework on Java Layer
APK File(Your Application)
(Java & C/C++)
Application Framework
Layer (Java)
Library Layer
(C/C++)
Kernel/Driver Layer
(C/ASM)
Call as Java API
Call as JNI(C/C++)
Call as SysCall(C/ASM)
Call Stack

## Slide 38
How to Add New APIs

## Slide 39: Application Framework Layer
Packages by Android Framework
android.accessibilityservice
android.accounts
android.animation
android.app
android.app.admin
android.app.backup
android.appwidget
android.bluetooth
android.content
android.content.pm
android.content.res
android.database
android.database.sqlite
android.drm
android.gesture
android.graphics
android.graphics.drawable
android.graphics.drawable.shapes
android.graphics.pdf
android.hardware
android.hardware.display
android.hardware.input
android.hardware.location
android.hardware.usb
android.inputmethodservice
android.location
android.media
android.media.audiofx
android.media.effect
android.mtp
android.net
android.net
android.net.http
android.net.nsd
android.net.rtp
android.net.sip
android.net.wifi
android.net.wifi.p2p
android.net.wifi.p2p.nsd
android.nfc
android.nfc.cardemulation
android.nfc.tech
android.opengl
android.os
android.os.storage
android.preference
android.print
android.print.pdf
android.printservice
android.provider
android.renderscript
android.sax
android.security
android.service.dreams
android.service.notification
android.service.textservice
android.service.wallpaper
android.speech
android.speech.tts
android.support.v13.app
android.support.v4.accessibilityservice
android.support.v4.app
android.support.v4.content
android.support.v4.content.pm
android.support.v4.database
android.support.v4.graphics.drawable
android.support.v4.hardware.display
android.support.v4.media
android.support.v4.net
android.support.v4.os
android.support.v4.print
android.support.v4.text
android.support.v4.util
android.support.v4.view
android.support.v4.view.accessibility
android.support.v4.widget
android.support.v7.app
android.support.v7.appcompat
android.support.v7.gridlayout
android.support.v7.media
android.support.v7.mediarouter
android.support.v7.view
android.support.v7.widget
android.support.v8.renderscript
android.telephony
android.telephony.cdma
android.telephony.gsm
android.test
android.test.mock
android.test.suitebuilder
android.text
android.text.format
android.text.method
android.text.style
android.text.util
android.transition
android.util
android.view
android.view.accessibility
android.view.animation
android.view.inputmethod
android.view.textservice
android.webkit
android.widget
dalvik.bytecode
dalvik.system

## Slide 40: Goal
Add “Calculator” API into Android System
  Package Name: itri.lecture
  Class Name: Cal
  Method
    int add(int, int)
    int sub(int, int)
  Android System
    Nexus7
    AOSP based Android 4.3.1

## Slide 41: Source Code of MyAPI
Java
  itri.lecture.Cal.java
    Main Program
  package.html, package-info.java
    Appoint about Build Target Dir
  package itri.lecture;
  public class Cal {
  public Cal() {}
  public static int add(int a, int b) {return a+b;}
  public int sub(int a, int b) {return a-b;}
  }
  <HTML><BODY>
  MyAPI Test Class.
  </BODY></HTML>
  package itri.lecture;

## Slide 42: Makefile of MyAPI
Android.mk
  Makefile for Android
    BUILD_JAVA_LIBRARY => Make .jar Package
    BUILD_SHARED_LIBRARY => Make .so Package
    BUILD_STATIC_LIBRARY => Make .a file
    BUILD_EXECUTABLE => Make ELF file (Executable file)
    BUILD_DROIDDOC => Make JavaDoc
  LOCAL_PATH := $(call my-dir)
  include $(CLEAR_VARS)
  LOCAL_SRC_FILES := $(call all-java-files-under, src)
  LOCAL_NO_STANDARD_LIBRARIES := true
  LOCAL_JAVA_LIBRARIES := core framework
  LOCAL_JAVACFLAGS := $(local_javac_flags)
  LOCAL_MODULE := myapi
  include $(BUILD_JAVA_LIBRARY)

## Slide 43: Makefile of MyAPI
Common.mk
  Used by Other .mk file besides MyAPI’s .mk .
    Ex. Framework Base’s Android.mk
CleanSpec.mk
  Newer Clean steps must be at the end of the list.
  # List of source to build into the myapi
  #
  core-myapi-files := \
  src/itri/lecture/Cal.java
  # List of junit javadoc source files for Android public API
  #
  # $(1): directory for search (to support use from frameworks/base)
  define myapi_to_document
  $(core-myapi-files)
  endef

## Slide 44: build/envsetup.sh
Helper Command Lib for Android Build
  m
    Build from Top Dir
  mm
    Build from Current Dir
  mmm [Target Dir]
    Build from Target Dir
  croot
    Change Top Dir
  cgrep
    Grep for C/C++ Source Code
  jgrep
    Grep for Java Source Code
  resgrep
    Grep for XML Source Code
  lunch
    Choose Target Build

## Slide 45: Setup Source Code of MyAPI
Copy to “framework” Directory
“framework/base” Directory
“framework/base/core” Directory

## Slide 46: Application Framework Layer
Packages by Android Framework
android.accessibilityservice
android.accounts
android.animation
android.app
android.app.admin
android.app.backup
android.appwidget
android.bluetooth
android.content
android.content.pm
android.content.res
android.database
android.database.sqlite
android.drm
android.gesture
android.graphics
android.graphics.drawable
android.graphics.drawable.shapes
android.graphics.pdf
android.hardware
android.hardware.display
android.hardware.input
android.hardware.location
android.hardware.usb
android.inputmethodservice
android.location
android.media
android.media.audiofx
android.media.effect
android.mtp
android.net
android.net
android.net.http
android.net.nsd
android.net.rtp
android.net.sip
android.net.wifi
android.net.wifi.p2p
android.net.wifi.p2p.nsd
android.nfc
android.nfc.cardemulation
android.nfc.tech
android.opengl
android.os
android.os.storage
android.preference
android.print
android.print.pdf
android.printservice
android.provider
android.renderscript
android.sax
android.security
android.service.dreams
android.service.notification
android.service.textservice
android.service.wallpaper
android.speech
android.speech.tts
android.support.v13.app
android.support.v4.accessibilityservice
android.support.v4.app
android.support.v4.content
android.support.v4.content.pm
android.support.v4.database
android.support.v4.graphics.drawable
android.support.v4.hardware.display
android.support.v4.media
android.support.v4.net
android.support.v4.os
android.support.v4.print
android.support.v4.text
android.support.v4.util
android.support.v4.view
android.support.v4.view.accessibility
android.support.v4.widget
android.support.v7.app
android.support.v7.appcompat
android.support.v7.gridlayout
android.support.v7.media
android.support.v7.mediarouter
android.support.v7.view
android.support.v7.widget
android.support.v8.renderscript
android.telephony
android.telephony.cdma
android.telephony.gsm
android.test
android.test.mock
android.test.suitebuilder
android.text
android.text.format
android.text.method
android.text.style
android.text.util
android.transition
android.util
android.view
android.view.accessibility
android.view.animation
android.view.inputmethod
android.view.textservice
android.webkit
android.widget
dalvik.bytecode
dalvik.system

## Slide 47: Add MyAPI’s Source Code Path
frameworks/base/Android.mk
  Base System for Framework(API)
  # Common sources for doc check and api check
  common_src_files := \
  $(call find-other-html-files, $(html_dirs)) \
  $(addprefix ../../libcore/, $(call libcore_to_document, $(LOCAL_PATH)/../../libcore)) \
  $(addprefix ../../external/junit/, $(call junit_to_document, $(LOCAL_PATH)/../../external/junit)) \
  $(addprefix ../../frameworks/myapi/, $(call myapi_to_document, $(LOCAL_PATH)/../../frameworks/myapi))
  # include definition of junit_to_document
  include external/junit/Common.mk
  # include definition of myapi_to_document
  include frameworks/myapi/Common.mk

## Slide 48: Set Target Product
build/target/product/mini.mk
build/target/product/core.mk
  # Base modules (will move elsewhere, previously user tagged)
  PRODUCT_PACKAGES += \
  20-dns.conf \
  95-configured \
  am \
  myapi \

## Slide 49: Set Class Path
system/core/rootdir/init.rc
build/core/dex_preopt.mk
  export BOOTCLASSPATH /system/framework/core.jar:/system/framework/core-junit.jar:/system/framework/bouncycastle.jar:/system/framework/ext.jar:/system/framework/framework.jar:/system/framework/telephony-common.jar:/system/framework/voip-common.jar:/system/framework/mms-common.jar:/system/framework/android.policy.jar:/system/framework/services.jar:/system/framework/apache-xml.jar:/system/framework/myapi.jar
  # TODO: replace it with device's BOOTCLASSPATH
  DEXPREOPT_BOOT_JARS := core:core-junit:bouncycastle:ext:myapi:framework:

## Slide 50: Make OTA image
Make OTA image
  This OTA image is update image for Android.
  This file name is
    aosp_flo-ota-eng.[your Linux’s User name].zip
  cd ~/nexus_work/android/
  source build/envsetup.sh
  lunch aosp_flo-user
  make otapackage

## Slide 51: What’s Android OTA-Package
Android OTA-Package has ROM images.
  boot.img
    Kernel, Init, Minimam Linux
  recovery.img
    Recovery Manager Program
  system.img
    Android System
  userdata.img
    User Data
Separated by Address

## Slide 52
How to Use New APIs

## Slide 53: No API on SDK…

## Slide 54: Setup API Version for MyAPI 1/2
development/sdk/api-versions.xml
  <class name="itri/lecture/Cal" since="18">
  <method name="&lt;init>()V" />
  <method name="add(II)I" />
  <method name="sub(II)I" />
  </class>

## Slide 55: Setup API Version for MyAPI 2/2
prebuilts/sdk/api/18.txt
  package itri.lecture {
  public class Cal {
  ctor public Cal();
  method public int add(int, int);
  method public static int sub(int, int);
  }
  }

## Slide 56: Setup JavaDoc
build/core/droiddoc.mk
  ifneq ($(LOCAL_SDK_VERSION),)
  ifeq ($(LOCAL_SDK_VERSION)$(TARGET_BUILD_APPS),current)
  # Use android_stubs_current if LOCAL_SDK_VERSION is current and no TARGET_BUILD_APPS.
  LOCAL_JAVA_LIBRARIES := android_stubs_current $(LOCAL_JAVA_LIBRARIES)
  else
  LOCAL_JAVA_LIBRARIES := sdk_v$(LOCAL_SDK_VERSION) $(LOCAL_JAVA_LIBRARIES)
  endif
  else
  LOCAL_JAVA_LIBRARIES := core ext framework myapi $(LOCAL_JAVA_LIBRARIES)
  endif # LOCAL_SDK_VERSION

## Slide 57: Make MySDK
Make MySDK
  This file name is
    android-sdk_eng.[your Linux’s User name]_linux-x86.zip
  cd ~/nexus_work/android/
  source build/envsetup.sh
  lunch sdk-eng
  make sdk

## Slide 58
How to Use New APIs

## Slide 59: Copy SDK to your Environment
“sdk/platforms/android-4.3.1”
to your “sdk/platforms/”

## Slide 60
How to Add New Library

## Slide 61: Library Layer
aac
android-clat
android-mock
ant-glob
antlr
apache-harmony
apache-http
apache-qp
apache-xml
arduino
bison
blktrace
bluetooth
bouncycastle
bsdiff
bzip2
ceres-solver
checkpolicy
chromium
chromium-libpac
chromium-trace
chromium_org
clang
compiler-rt
dexmaker
dhcpcd
dnsmasq
doclava
droiddriver
dropbear
e2fsprogs
easymock
eclipse-basebuilder
eclipse-windowbuilder
eigen
elfutils
embunit
emma
esd
expat
eyes-free
fdlibm
flac
freetype
fsck_msdos
ganymed-ssh2
gcc-demangle
genext2fs
giflib
google-diff-match-patch
grub
gtest
guava
hamcrest
harfbuzz
harfbuzz_ng
hyphenation
icu4c
iproute2
ipsec-tools
iptables
iputils
jack
javasqlite
javassist
jdiff
jhead
jmdns
jmonkeyengine
jpeg
jsilver
jsr305
junit
kernel-headers
libcap-ng
libffi
libgsm
liblzf
libmtp
libnfc-nci
libnfc-nxp
libnl-headers
libogg
libpcap
libphonenumber
libpng
libppp
libselinux
libsepol
libusb
libusb-compat
libvorbis
libvpx
Linux Software & Linux Library
libxml2
libxslt
libyuv
linux-tools-perf
littlemock
llvm
lzma
marisa-trie
markdown
mdnsresponder
mesa3d
mksh
mockito
mockwebserver
mp4parser
mtpd
naver-fonts
netcat
netperf
neven
nist-pkits
nist-sip
noto-fonts
oauth
objenesis
okhttp
open-vcdiff
opencv
openfst
openssh
openssl
oprofile
pixman
ppp
proguard
protobuf
qemu
qemu-pc-bios
regex-re2
replicaisland
robolectric
safe-iop
scrypt
sepolicy
sfntly
sil-fonts
skia
smack
smali
sonivox
speex
sqlite
srec
srtp
stlport
strace
stressapptest
svox
tagsoup
tcpdump
timezonepicker-support
tinyalsa
tinycompress
tinyxml
tinyxml2
tremolo
v8
valgrind
webp
webrtc
wpa_supplicant_8
xmlwriter
xmp_toolkit
yaffs2
zlib
zxing

## Slide 62: How to Develop?
NDK wo/ADT
  Standard Android Application for C/C++
  Only C/C++ on Limited Library Layer
Advantage
  Only C/C++
  DirectCall C/C++ API
Dis-Advantage
  Use a few Android Tools
  A few Docs from Google Developer Site & Blogs
APK File(Your Application)
(C/C++)
Library Layer
(C/C++)
Kernel/Driver Layer
(C/ASM)
Call as C/C++ APIs
Call as SysCall(C/ASM)
Call Stack

## Slide 63
How to Build OpenCV for Android

## Slide 64: Download OpenCV & NDK tool
  wget https://github.com/Itseez/opencv/archive/2.4.7.tar.gz
  tar zxfv 2.4.7.tar.gz
  mkdir ~/android/
  cd ~/android/
  wget http://dl.google.com/android/android-sdk_r22.3-linux.tgz
  wget http://dl.google.com/android/ndk/android-ndk-r8e-linux-x86_64.tar.bz2
  tar zxfv android-sdk_r22.3-linux.tgz
  tar jxfv android-ndk-r8e-linux-x86_64.tar.bz2

## Slide 65: Edit Setup File
Add Android Source Code directory.
  ~/opencv-2.4.7/platforms/scripts/cmake_android_service.sh
    -DANDROID_SOURCE_TREE=~/nexus_work/android/
  cmake -DCMAKE_TOOLCHAIN_FILE=../android/android.toolchain.cmake -DANDROID_TOOLCHAIN_NAME="arm-linux-androideabi-4.4.3" -DANDROID_STL=stlport_static -DANDROID_STL_FORCE_FEATURES=OFF -DBUILD_ANDROID_SERVICE=ON -DANDROID_SOURCE_TREE=~/Projects/AndroidSource/ServiceStub/ $@ ../..

## Slide 66: Set Path to SDK/NDK
  export ANDROID_NDK=~/android/android-ndk-r8e
  export ANDROID_SDK=~/android/android-sdk-linux

## Slide 67: Make Version File
Require “AndroidCamera” Func.
Edit Version Number
  cp -v ~/nexus_work/android/development/sdk/platform_source.prop_template ~/nexus_work/android/development/sdk/platform_source.properties
  Platform.Version=4.3.1

## Slide 68: Copy some haeder files & so Libs
Require “AndroidCamera” Func.
  cp -aR ~/android/android-ndk-r8e/platforms/android-14/arch-arm/usr/include/EGL ~/opencv-2.4.7/modules/androidcamera/include/
  cp -v ~/nexus_work/android/out/target/product/flo/system/lib/libbinder.so $(ANDROID_NDK)/platforms/android-8/arch-arm/usr/lib/
  cp -v ~/nexus_work/android/out/target/product/flo/system/lib/libutils.so $(ANDROID_NDK)/platforms/android-8/arch-arm/usr/lib/
  cp -v ~/nexus_work/android/out/target/product/flo/system/lib/libandroid_runtime.so $(ANDROID_NDK)/platforms/android-8/arch-arm/usr/lib/

## Slide 69: Modify Compile Option
~/opencv-2.4.7/modules/androidcamera/CMakeLists.txt
  function(replace_compiler_option var old new)
  # Replaces a compiler option or switch old in var by new.
  # If old is not in var, appends new to var.
  # Example: replace_compiler_option(CMAKE_CXX_FLAGS_RELEASE "-O3" "-O2")
  # If the option already is on the variable, don't add it:
  if( "${${var}}" MATCHES "(^| )${new}($| )" )
  set(n "")
  else()
  set(n "${new}")
  endif()
  if( "${${var}}" MATCHES "(^| )${old}($| )" )
  string( REGEX REPLACE "(^| )${old}($| )" " ${n} " ${var} "${${var}}" )
  else()
  set( ${var} "${${var}} ${n}" )
  endif()
  set( ${var} "${${var}}" PARENT_SCOPE )
  endfunction(replace_compiler_option)
  replace_compiler_option(CMAKE_CXX_FLAGS "-frtti" "-fno-rtti")
  status("camera_wrapper C++ flags):" ${CMAKE_CXX_FLAGS})

## Slide 70: Include new Include File Dir
Android 4.3’s Include File Dir was separated.
  ~/opencv-2.4.7/platforms/android/service/engine/CMakeLists.txt
  include_directories(SYSTEM "${ANDROID_SOURCE_TREE}/frameworks/base/include" "${ANDROID_SOURCE_TREE}/system/core/include") "${ANDROID_SOURCE_TREE}/frameworks/native/include/"

## Slide 71: Delete "DetectTegra“ Func
This Android System doesn't have "Tegra“.
  ~/opencv-2.4.7/platforms/android/service/engine/jni/BinderComponent/TegraDetector.h
  int DetectTegra(){};
      ↓
  int DetectTegra(){return NOT_TEGRA;};

## Slide 72: Make Define Log Func
Android Logging System was Changed…
  Make 『FakeLog.h』 file
    ~/opencv-2.4.7/platform/android/service/engine/jni/include/
  #ifndef __FAKE_LOG_H__
  #define __FAKE_LOG_H__
  #define LOGD ALOGD
  #define LOGI ALOGI
  #define LOGE ALOGE
  #endif

## Slide 73: Include Fake Log Header
  ~/opencv-2.4.7/platform/android/service/engine/jni/
    BinderComponent/BnOpenCVEngine.h
    BinderComponent/HardwareDetector.h
    JNIWrapper/JavaBasedPackageManager.h
    JNIWrapper/OpenCVLibraryInfo.h
  #include "FakeLog.h"

## Slide 74: Execute Auto Config & make
This Script make Makefile for OpenCV.
  In “~/opencv-2.4.7/platforms/scripts/build_android_service”
Make !!!
  cd ~/opencv-2.4.7/platforms/scripts/
  ./cmake_android_service.sh
  cd ~/opencv-2.4.7/platforms/scripts/build_android_service/
  make

## Slide 75: Where are Made Files?
OpenCV Libs.
  In “~/opencv-2.4.7/platforms/build_android_service/lib”
    highgui
    core
    etc...
3rd Party Libs for OpenCV.
  In “~/opencv-2.4.7/platforms/build_android_service/3rdparty/lib”
    libIlmImf
    libjasper
    libjpeg
    libpng
    libtiff

## Slide 76
How to Use OpenCV for Android

## Slide 77: Native Application
NDK wo/ADT
  Standard Android Application for C/C++
  Only C/C++ on Limited Library Layer
Advantage
  Only C/C++
  DirectCall C/C++ API
Dis-Advantage
  Use a few Android Tools
  A few Docs from Google Developer Site & Blogs
APK File(Your Application)
(C/C++)
Library Layer
(C/C++)
Kernel/Driver Layer
(C/ASM)
Call as C/C++ APIs
Call as SysCall(C/ASM)
Call Stack

## Slide 78: Use NativeActivity of OpenCV
This Sample uses Only C/C++ Code.
  ~/opencv-2.4.7/samples/android/native-activity
Structure of NativeActivity
  AndroidManifest.xml <- Property File for Android
  res <- Directory that has Resource file(Image,Voice)
  jni <- Directory that has files for NDK
    Android.mk <- make file of NDK
    Application.mk <- property file of NDK
    native.cpp <- Sample App
  Other Files/Dir, don’t use.

## Slide 79: Edit AndroidManifest.xml
Replace “application” Section
  <application android:label="@string/app_name" android:hasCode="false">
  <activity android:name="android.app.NativeActivity"
  android:label="@string/app_name"
  android:configChanges="orientation|keyboardHidden">
  <!-- Tell NativeActivity the name of or .so -->
  <meta-data android:name="android.app.lib_name"
  android:value="native_activity" />
  <intent-filter>
  <action android:name="android.intent.action.MAIN" />
  <category android:name="android.intent.category.LAUNCHER" />
  </intent-filter>
  </activity>
  </application>

## Slide 80: About AndroidManifest.xml
API Level
Permission
  <!-- This is the platform API where NativeActivity was introduced. -->
  <uses-sdk android:minSdkVersion=“9" />
  <uses-permission android:name="android.permission.CAMERA"/>

## Slide 81: Edit jni/Application.xml
Change STL Lib
API Level
  APP_STL := gnustl_static
  ↓
  APP_STL := stlport_static
  APP_PLATFORM := android-9

## Slide 82: Edit jni/Android.mk 1/8
Delete
Set OpenCV Libs
  include ../../sdk/native/jni/OpenCV.mk
  OPENCV_MODULES:=contrib legacy ml stitching objdetect ts videostab video photo calib3d features2d highgui imgproc flann core androidcamera

## Slide 83: Edit jni/Android.mk 2/8
Make Loading OpenCV Libs Function
  $(foreach module,$(OPENCV_MODULES),$(eval $(call add_opencv_module,$(module))))
  define add_opencv_module
  include $(CLEAR_VARS)
  LOCAL_MODULE:=opencv_$1
  LOCAL_SRC_FILES:=../../opencv-2.4.7/platforms/build_android_service/lib/armeabi-v7a/libopencv_$1.a
  include $(PREBUILT_STATIC_LIBRARY)
  endef

## Slide 84: Edit jni/Android.mk 3/8
Set 3rd Party Libs for OpenCV
  OPENCV_3RDPARTY_COMPONENTS:=libjpeg libpng libtiff libjasper IlmImf

## Slide 85: Edit jni/Android.mk 4/8
Make Loading OpenCV Libs Function
  $(foreach module,$(OPENCV_3RDPARTY_COMPONENTS),$(eval $(call add_opencv_3rdparty_component,$(module))))
  define add_opencv_3rdparty_component
  include $(CLEAR_VARS)
  LOCAL_MODULE:=$1
  LOCAL_SRC_FILES:=../../opencv-2.4.7/platforms/build_android_service/3rdparty/lib/armeabi-v7a/lib$1.a
  include $(PREBUILT_STATIC_LIBRARY)
  endef

## Slide 86: Edit jni/Android.mk 5/8
Set AndroidCamera Libs for OpenCV
  OPENCV_CAMERA_MODULES:= native_camera_r2.2.0 native_camera_r2.3.3 native_camera_r3.0.1 native_camera_r4.0.0 native_camera_r4.0.3 native_camera_r4.1.1 native_camera_r4.2.0 native_camera_r4.3.0

## Slide 87: Edit jni/Android.mk 6/8
Make Loading AndroidCamera Libs Function
  $(foreach module,$(OPENCV_CAMERA_MODULES),$(eval $(call add_opencv_camera_module,$(module))))
  define add_opencv_camera_module
  include $(CLEAR_VARS)
  LOCAL_MODULE:=$1
  LOCAL_SRC_FILES:=../../opencv-2.4.7/platforms/build_android_service/lib/armeabi-v7a/lib$1.so
  include $(PREBUILT_SHARED_LIBRARY)
  endef

## Slide 88: Edit jni/Android.mk 7/8
Add Magic Word for Reset
Set Include Dir
  include $(CLEAR_VARS)
  OPENCV_INCLUDE_DIR:=$(LOCAL_DIR)/../opencv-2.4.7/include
  LOCAL_C_INCLUDES+=$(OPENCV_INCLUDE_DIR)/opencv $(OPENCV_INCLUDE_DIR)/opencv2 ../opencv-2.4.7/modules/stitching/include ../opencv-2.4.7/modules/objdetect/include ../opencv-2.4.7/modules/photo/include ../opencv-2.4.7/modules/flann/include ../opencv-2.4.7/modules/core/include ../opencv-2.4.7/modules/ts/include ../opencv-2.4.7/modules/highgui/include ../opencv-2.4.7/modules/contrib/include ../opencv-2.4.7/modules/video/include ../opencv-2.4.7/modules/imgproc/include ../opencv-2.4.7/modules/legacy/include ../opencv-2.4.7/modules/ocl/include ../opencv-2.4.7/modules/features2d/include ../opencv-2.4.7/modules/calib3d/include ../opencv-2.4.7/modules/ml/include ../opencv-2.4.7/modules/videostab ../opencv-2.4.7/modules/nonfree/include ../opencv-2.4.7/modules/androidcamera/include

## Slide 89: Edit jni/Android.mk 8/8
Add Loading Lib & OpenCV Lib
  LOCAL_LDLIBS
    -lc -ldl -lz
  LOCAL_STATIC_LIBRARIES
    $(foreach mod, $(OPENCV_MODULES), opencv_$(mod)) $(OPENCV_3RDPARTY_COMPONENTS)
  LOCAL_LDLIBS += -lm -llog -landroid -lc -ldl -lz
  LOCAL_STATIC_LIBRARIES := android_native_app_glue $(foreach mod, $(OPENCV_MODULES), opencv_$(mod)) $(OPENCV_3RDPARTY_COMPONENTS)

## Slide 90: Setup/Make Build.xml 1/2
Making Setting File for Android using ANT
  Today, Development on CUI Only!!!
    Don’t use Eclipse!
  android list target
    Available Android targets:
    ----------
    id: 1 or "android-9"
    Name: Android 2.3.1
    Type: Platform
    API level: 9
    Revision: 2
    Skins: WQVGA400, QVGA, HVGA, WVGA800 (default), WVGA854
    ABIs : armeabi
    ----------
    id: 2 or "android-18"
    Name: Android 4.3
    Type: Platform
    API level: 18
    Revision: 2
    Skins: WXGA800, WQVGA400, QVGA, WQVGA432, WXGA800-7in, WVGA800 (default), HVGA, WXGA720, WSVGA, WVGA854
    ABIs : armeabi-v7a
    ----------

## Slide 91: Setup/Make Build.xml 2/2
Make Build.xml
  android update project --path . --target 2

## Slide 92: Build NativeActivity
Build C/C++ Source Codes
Make APK File
  ndk-build [clean all]
  ant [debug|release]

## Slide 93: Install NativeActivity.apk
Install APK File
UnInstall APK File
Show Log
  adb install bin/NativeActivity-debug.apk
  adb logcat
  adb uninstall com.example.native_activity

## Slide 94: adb(Android Debug Bridge)
Functions
  Shell on Android Device
    adb shell
  Show Connected Android Devices
    adb devices
  Install/Uninstall APK File
    adb install/uninstall [App Name]/[Package Name]
  Send/Get File to/from Android Device
    adb push/pull [from File Path] [to File Path]
  Show Log (DDMS)
    adb logcat

## Slide 95
How About NativeActivity

## Slide 96: Quick Explanation to NativeActivity
How to Use Camera
  struct Engine
  {
  android_app* app;
  cv::Ptr<cv::VideoCapture> capture;
  };
  （snip）
  cv::Mat drawing_frame;
  (snip)
  engine.capture->retrieve(drawing_frame, CV_CAP_ANDROID_COLOR_FRAME_RGBA);
  char buffer[256];
  sprintf(buffer, "Display performance: %dx%d @ %.3f", drawing_frame.cols, drawing_frame.rows, fps);
  cv::putText(drawing_frame, std::string(buffer), cv::Point(8,64),
  cv::FONT_HERSHEY_COMPLEX_SMALL, 1, cv::Scalar(0,255,0,255));
  engine_draw_frame(&engine, drawing_frame);

## Slide 97: Quick Explanation to NativeActivity
Event Driven Code for Android
  static void engine_handle_cmd(android_app* app, int32_t cmd)
  {
  Engine* engine = (Engine*)app->userData;
  switch (cmd)
  {
  （snip）
  void android_main(android_app* app)
  {
  Engine engine;
  // Make sure glue isn't stripped.
  app_dummy();
  size_t engine_size = sizeof(engine);
  memset((void*)&engine, 0, engine_size);
  app->userData = &engine;
  app->onAppCmd = engine_handle_cmd;
  engine.app = app;
  （snip）

## Slide 98: LifeCycle Diagram
Activity is Event Driven Arch
Main Event
  onCreate()
    Start Activity
    Initialize Objects
  onStart()
    Finish Initialized
  onPause()
    Other Activity Start
  onResume()
    Back from Other Activity
  onStop()
    Don’t back long time

## Slide 99: But…
Some Android Camera doesn’t work…
#if !defined(ANDROID_r2_2_0) &&
!defined(ANDROID_r2_3_3) &&
!defined(ANDROID_r3_0_1) &&
!defined(ANDROID_r4_0_0) &&
!defined(ANDROID_r4_0_3) &&
!defined(ANDROID_r4_1_1) &&
!defined(ANDROID_r4_2_0) &&
!defined(ANDROID_r4_3_0)
# error Building camera wrapper for your version of Android is not supported by OpenCV.\
You need to modify OpenCV sources in order to compile camera wrapper for your version of Android.
#endif

## Slide 100: Android Camera for Java
android.hardware.Camera
  Android Framework’s Class
libcameraservice.so
libcamera_client.so
  Absorption for Camera
CameraHardwareInterface
  Hardware Camera
android.hardware.Camera
(Java)
libCameraService.so
(C/C++)
CameraHardwareInterface
(C/ASM)
Call as Android API
libCamera_Client.so
(C/C++)
Call as Shared Lib
Call as ko Lib

## Slide 101: Android Camera for OpenCV
Directly Call
  Libcamera_client.so
Maybe Because…
  They avoid overhead in
    libcameraservice.so
    libcamera_client.so
  However…
    Their Coding is original,
    Some Devices don’t work.
native_camera_rx.x.x.so
(C/C++)
CameraHardwareInterface
(C/ASM)
libCamera_Client.so
(C/C++)
Call as Shared Lib
Call as ko Lib

## Slide 102
How to Add New Driver

## Slide 103: Kernel/Driver Layer
Android Source Tree
  Ex. Nexus7(2013)
  Device
    Asus
      flo
      flo-kernel
  Hardware
    Qcom
      audio
      bt
      camera
      display
      keymaster
      media
      msm8960
      msm8x74
      power
      sensors
      wlan

## Slide 104
How to Add V4L for OpenCV

## Slide 105: Why?
OpenCV for Android doesn’t have “V4L”.
  It use Android build-in Camera.
Except Phone/Table don’t have Camera…
  You MUST customize OpenCV for Android.

## Slide 106: Add New UVC Driver
drivers/media/video/uvc/uvc_driver.c
  Add after “static struct usb_device_id uvc_ids[] = {“
  /* Etron Tech */
  { .match_flags = USB_DEVICE_ID_MATCH_DEVICE
  | USB_DEVICE_ID_MATCH_INT_INFO,
  .idVendor = 0x1e4e,
  .idProduct = 0x0104,
  .bInterfaceClass = USB_CLASS_VIDEO,
  .bInterfaceSubClass = 1,
  .bInterfaceProtocol = 0,
  .driver_info = UVC_QUIRK_PROBE_MINMAX },

## Slide 107: Download & Build kernel
Download & Build kernel
  cd ~/nexus_work
  export ARCH=arm
  export CROSS_COMPILE=~/nexus_work/android/prebuilts/gcc/linux-x86/arm/arm-eabi-4.6/bin/arm-eabi-
  git clone https://android.googlesource.com/kernel/msm.git -b android-msm-flo-3.4-jb-mr2 kernel/nexus72
  cd kernel/nexus72
  make flo_defconfig
  make menuconfig
  make
  cp arch/arm/boot/zImage ~/nexus_work/android/device/asus/flo-kernel/kernel

## Slide 108: Change Permission
android/device/asus/flo/ueventd.flo.rc
  Change “/dev/video*” Permission
  /dev/video* 0666 system camera

## Slide 109: Re-Make OTA image
Re-Make OTA image
  Require “clean”, because “init.*” doesn’t update.
  This file name is
    aosp_flo-ota-eng.[your Linux’s User name].zip
  cd ~/nexus_work/android/
  source build/envsetup.sh
  lunch aosp_flo-user
  make clean
  make otapackage

## Slide 110
How to Build OpenCV for V4L
Almost Same in “for Android”
Same Pages are Gray Out

## Slide 111: Download OpenCV & NDK tool
  wget https://github.com/Itseez/opencv/archive/2.4.7.tar.gz
  tar zxfv 2.4.7.tar.gz
  mkdir ~/android/
  cd ~/android/
  wget http://dl.google.com/android/android-sdk_r22.3-linux.tgz
  wget http://dl.google.com/android/ndk/android-ndk-r8e-linux-x86_64.tar.bz2
  tar zxfv android-sdk_r22.3-linux.tgz
  tar jxfv android-ndk-r8e-linux-x86_64.tar.bz2

## Slide 112: Edit Setup File
Add Android Source Code directory.
  ~/opencv-2.4.7/platforms/scripts/cmake_android_service.sh
    -DANDROID_SOURCE_TREE=~/nexus_work/android/
  cmake -DCMAKE_TOOLCHAIN_FILE=../android/android.toolchain.cmake -DANDROID_TOOLCHAIN_NAME="arm-linux-androideabi-4.4.3" -DANDROID_STL=stlport_static -DANDROID_STL_FORCE_FEATURES=OFF -DBUILD_ANDROID_SERVICE=ON -DANDROID_SOURCE_TREE=~/Projects/AndroidSource/ServiceStub/ $@ ../..

## Slide 113: Set Path to SDK/NDK
  export ANDROID_NDK=~/android/android-ndk-r8e
  export ANDROID_SDK=~/android/android-sdk-linux

## Slide 114: Make Version File
Require “AndroidCamera” Func.
Edit Version Number
  cp -v ~/nexus_work/android/development/sdk/platform_source.prop_template ~/nexus_work/android/development/sdk/platform_source.properties
  Platform.Version=4.3.1

## Slide 115: Copy some haeder files & so Libs
Require “AndroidCamera” Func.
  cp -aR ~/android/android-ndk-r8e/platforms/android-14/arch-arm/usr/include/EGL ~/opencv-2.4.7/modules/androidcamera/include/
  cp -v ~/nexus_work/android/out/target/product/flo/system/lib/libbinder.so $(ANDROID_NDK)/platforms/android-8/arch-arm/usr/lib/
  cp -v ~/nexus_work/android/out/target/product/flo/system/lib/libutils.so $(ANDROID_NDK)/platforms/android-8/arch-arm/usr/lib/
  cp -v ~/nexus_work/android/out/target/product/flo/system/lib/libandroid_runtime.so $(ANDROID_NDK)/platforms/android-8/arch-arm/usr/lib/

## Slide 116: Include new Include File Dir
Android 4.3’s Include File Dir was separated.
  ~/opencv-2.4.7/platforms/android/service/engine/CMakeLists.txt
  include_directories(SYSTEM "${ANDROID_SOURCE_TREE}/frameworks/base/include" "${ANDROID_SOURCE_TREE}/system/core/include") "${ANDROID_SOURCE_TREE}/frameworks/native/include/"

## Slide 117: Delete "DetectTegra“ Func
This Android System doesn't have "Tegra“.
  ~/opencv-2.4.7/platforms/android/service/engine/jni/BinderComponent/TegraDetector.h
  int DetectTegra(){};
      ↓
  int DetectTegra(){return NOT_TEGRA;};

## Slide 118: Make Define Log Func
Android Logging System was Changed…
  Make 『FakeLog.h』 file
    ~/opencv-2.4.7/platform/android/service/engine/jni/include/
  #ifndef __FAKE_LOG_H__
  #define __FAKE_LOG_H__
  #define LOGD ALOGD
  #define LOGI ALOGI
  #define LOGE ALOGE
  #endif

## Slide 119: Include Fake Log Header
  ~/opencv-2.4.7/platform/android/service/engine/jni/
    BinderComponent/BnOpenCVEngine.h
    BinderComponent/HardwareDetector.h
    JNIWrapper/JavaBasedPackageManager.h
    JNIWrapper/OpenCVLibraryInfo.h
  #include "FakeLog.h"

## Slide 120: Comment Out AndroidCamera 1/2
OpenCV for Android ONLY use AndroidCamera.
  ~/opencv-2.4.7/modules/highgui/CMakeLists.txt
    Change:
    Delete:
  ocv_add_module(highgui opencv_imgproc OPTIONAL opencv_androidcamera)
  ↓
  ocv_add_module(highgui opencv_imgproc)
  list(APPEND highgui_srcs src/cap_android.cpp)

## Slide 121: Comment Out AndroidCamera 2/2
OpenCV for Android ONLY use AndroidCamera.
  ~/opencv-2.4.7/modules/androidcamera/CMakeLists.txt
    Delete:
  ocv_module_disable(androidcamera)

## Slide 122: Comment in V4L 1/2
Enabel V4L in highgui.
  ~/opencv-2.4.7/modules/highgui/CMakeLists.txt
    Add:
  ~/opencv-2.4.7/modules/highgui/src/cap.cpp
    Add in under Functions:
    “CV_IMPL CvCapture * cvCreateCameraCapture (int index)”
  list(APPEND highgui_srcs src/cap_libv4l.cpp)
  list(APPEND highgui_srcs src/cap_v4l.cpp)
  return cvCreateCameraCapture_V4L (index);

## Slide 123: Comment in V4L 2/2
-DWITH_V4L=ON doesn't work...
  ~/opencv-2.4.7/modules/highgui/src/cap.cpp
  ~/opencv-2.4.7/modules/highgui/src/cap_libv4l.cpp
  #define HAVE_CAMV4L
  #define HAVE_CAMV4L2
  #define HAVE_LIBV4L

## Slide 124: Copy V4L Header Files
  cp -v /usr/include/libv4l1.h ~/opencv-2.4.7/modules/highgui/include/
  cp -v /usr/include/libv4l2.h ~/opencv-2.4.7/modules/highgui/include/
  cp -v /usr/include/libv4lconvert.h ~/opencv-2.4.7/modules/highgui/include/
  cp -v /usr/include/libv4l1-videodev.h ~/opencv-2.4.7/modules/highgui/include/

## Slide 125: Delete Java Lib
This Lib require AndroidCamera
  rm -fr ~/opencv-2.4.7/modules/java/

## Slide 126: Execute Auto Config & make
This Script make Makefile for OpenCV.
  In “~/opencv-2.4.7/platforms/scripts/build_android_service”
Make !!!
  cd ~/opencv-2.4.7/platforms/scripts/
  ./cmake_android_service.sh
  cd ~/opencv-2.4.7/platforms/scripts/build_android_service/
  make

## Slide 127: Where are Made Files?
OpenCV Libs.
  In “~/opencv-2.4.7/platforms/build_android_service/lib”
    highgui
    core
    etc...
3rd Party Libs for OpenCV.
  In “~/opencv-2.4.7/platforms/build_android_service/3rdparty/lib”
    libIlmImf
    libjasper
    libjpeg
    libpng
    libtiff

## Slide 128
How to Use OpenCV for V4L
Almost Same in “for Android”
Same Pages are Gray Out

## Slide 129: Use NativeActivity of OpenCV
This Sample uses Only C/C++ Code.
  ~/opencv-2.4.7/samples/android/native-activity
Structure of NativeActivity
  AndroidManifest.xml <- Property File for Android
  res <- Directory that has Resource file(Image,Voice)
  jni <- Directory that has files for NDK
    Android.mk <- make file of NDK
    Application.mk <- property file of NDK
    native.cpp <- Sample App
  Other Files/Dir, don’t use.

## Slide 130: Edit AndroidManifest.xml
Replace “application” Section
  <application android:label="@string/app_name" android:hasCode="false">
  <activity android:name="android.app.NativeActivity"
  android:label="@string/app_name"
  android:configChanges="orientation|keyboardHidden">
  <!-- Tell NativeActivity the name of or .so -->
  <meta-data android:name="android.app.lib_name"
  android:value="native_activity" />
  <intent-filter>
  <action android:name="android.intent.action.MAIN" />
  <category android:name="android.intent.category.LAUNCHER" />
  </intent-filter>
  </activity>
  </application>

## Slide 131: About AndroidManifest.xml
API Level
Permission
  <!-- This is the platform API where NativeActivity was introduced. -->
  <uses-sdk android:minSdkVersion=“9" />
  <uses-permission android:name="android.permission.CAMERA"/>

## Slide 132: Edit jni/Application.xml
Change STL Lib
API Level
  APP_STL := gnustl_static
  ↓
  APP_STL := stlport_static
  APP_PLATFORM := android-9

## Slide 133: Edit jni/Android.mk 1/8
Delete
Set OpenCV Libs
  include ../../sdk/native/jni/OpenCV.mk
  OPENCV_MODULES:=contrib legacy ml stitching objdetect ts videostab video photo calib3d features2d highgui imgproc flann core androidcamera

## Slide 134: Edit jni/Android.mk 2/8
Make Loading OpenCV Libs Function
  $(foreach module,$(OPENCV_MODULES),$(eval $(call add_opencv_module,$(module))))
  define add_opencv_module
  include $(CLEAR_VARS)
  LOCAL_MODULE:=opencv_$1
  LOCAL_SRC_FILES:=../../opencv-2.4.7/platforms/build_android_service/lib/armeabi-v7a/libopencv_$1.a
  include $(PREBUILT_STATIC_LIBRARY)
  endef

## Slide 135: Edit jni/Android.mk 3/8
Set 3rd Party Libs for OpenCV
  OPENCV_3RDPARTY_COMPONENTS:=libjpeg libpng libtiff libjasper IlmImf

## Slide 136: Edit jni/Android.mk 4/8
Make Loading OpenCV Libs Function
  $(foreach module,$(OPENCV_3RDPARTY_COMPONENTS),$(eval $(call add_opencv_3rdparty_component,$(module))))
  define add_opencv_3rdparty_component
  include $(CLEAR_VARS)
  LOCAL_MODULE:=$1
  LOCAL_SRC_FILES:=../../opencv-2.4.7/platforms/build_android_service/3rdparty/lib/armeabi-v7a/lib$1.a
  include $(PREBUILT_STATIC_LIBRARY)
  endef

## Slide 137: Edit jni/Android.mk 7/8
Add Magic Word for Reset
Set Include Dir
  include $(CLEAR_VARS)
  OPENCV_INCLUDE_DIR:=$(LOCAL_DIR)/../opencv-2.4.7/include
  LOCAL_C_INCLUDES+=$(OPENCV_INCLUDE_DIR)/opencv $(OPENCV_INCLUDE_DIR)/opencv2 ../opencv-2.4.7/modules/stitching/include ../opencv-2.4.7/modules/objdetect/include ../opencv-2.4.7/modules/photo/include ../opencv-2.4.7/modules/flann/include ../opencv-2.4.7/modules/core/include ../opencv-2.4.7/modules/ts/include ../opencv-2.4.7/modules/highgui/include ../opencv-2.4.7/modules/contrib/include ../opencv-2.4.7/modules/video/include ../opencv-2.4.7/modules/imgproc/include ../opencv-2.4.7/modules/legacy/include ../opencv-2.4.7/modules/ocl/include ../opencv-2.4.7/modules/features2d/include ../opencv-2.4.7/modules/calib3d/include ../opencv-2.4.7/modules/ml/include ../opencv-2.4.7/modules/videostab ../opencv-2.4.7/modules/nonfree/include ../opencv-2.4.7/modules/androidcamera/include

## Slide 138: Edit jni/Android.mk 8/8
Add Loading Lib & OpenCV Lib
  LOCAL_LDLIBS
    -lc -ldl -lz
  LOCAL_STATIC_LIBRARIES
    $(foreach mod, $(OPENCV_MODULES), opencv_$(mod)) $(OPENCV_3RDPARTY_COMPONENTS)
  LOCAL_LDLIBS += -lm -llog -landroid -lc -ldl -lz
  LOCAL_STATIC_LIBRARIES := android_native_app_glue $(foreach mod, $(OPENCV_MODULES), opencv_$(mod)) $(OPENCV_3RDPARTY_COMPONENTS)

## Slide 139: Setup libv4l for Android
Download libv4l Lib for Android
Set libv4l Lib to NDK
  UnPacked & Copy to:
  $(ANDROID_NDK)/source/opencv/
  wget http://www.noritsuna.com/download/libv4l_for_android.tar.gz

## Slide 140: Edit jni/Android.mk Ext-1
Add libv4l Lib in:
Add import-module Func in Last Line
  LOCAL_STATIC_LIBRARIES := android_native_app_glue $(foreach mod, $(OPENCV_MODULES), opencv_$(mod)) $(OPENCV_3RDPARTY_COMPONENTS) opencv_libv4l
  $(call import-module,opencv/libv4l)

## Slide 141: Edit jni/Android.mk Ext-2
If you edited about “AndroidCamera” Libs,
Please Delete it!
Delete AndroidCamera Libs for OpenCV
  OPENCV_CAMERA_MODULES:= native_camera_r2.2.0 native_camera_r2.3.3 native_camera_r3.0.1 native_camera_r4.0.0 native_camera_r4.0.3 native_camera_r4.1.1 native_camera_r4.2.0 native_camera_r4.3.0

## Slide 142: Edit jni/Android.mk Ext-3
Delete Loading AndroidCamera Libs Function
  $(foreach module,$(OPENCV_CAMERA_MODULES),$(eval $(call add_opencv_camera_module,$(module))))
  define add_opencv_camera_module
  include $(CLEAR_VARS)
  LOCAL_MODULE:=$1
  LOCAL_SRC_FILES:=../../opencv-2.4.7/platforms/build_android_service/lib/armeabi-v7a/lib$1.so
  include $(PREBUILT_SHARED_LIBRARY)
  endef

## Slide 143: Setup/Make Build.xml 1/2
Making Setting File for Android using ANT
  Today, Development on CUI Only!!!
    Don’t use Eclipse!
  android list target
    Available Android targets:
    ----------
    id: 1 or "android-9"
    Name: Android 2.3.1
    Type: Platform
    API level: 9
    Revision: 2
    Skins: WQVGA400, QVGA, HVGA, WVGA800 (default), WVGA854
    ABIs : armeabi
    ----------
    id: 2 or "android-18"
    Name: Android 4.3
    Type: Platform
    API level: 18
    Revision: 2
    Skins: WXGA800, WQVGA400, QVGA, WQVGA432, WXGA800-7in, WVGA800 (default), HVGA, WXGA720, WSVGA, WVGA854
    ABIs : armeabi-v7a
    ----------

## Slide 144: Setup/Make Build.xml 2/2
Make Build.xml
  android update project --path . --target 2

## Slide 145: Build NativeActivity
Build C/C++ Source Codes
Make APK File
  ndk-build [clean all]
  ant [debug|release]

## Slide 146: Install NativeActivity.apk
Install APK File
UnInstall APK File
Show Log
  adb install bin/NativeActivity-debug.apk
  adb logcat
  adb uninstall com.example.native_activity

## Slide 147
How to Add New Native App

## Slide 148: How to Develop?
As Linux Application
  Non-Standard Android Application
  Full Linux C/C++ on Library Layer
Advantage
  Use Other Linux Libs
Dis-Advantage
  Must Modify Android System
    How to Modify on next Lecture
ELF File(Your Application)
(C/C++)
Library Layer + Linux Libs
(C/C++)
Kernel/Driver Layer
(C/ASM)
Call as C/C++ APIs
Call as SysCall(C/ASM)
Call Stack

## Slide 149: Make Execute File
Make Dir
  hello-exe/
  hello-exe/jni
Make Source Code: hello-exe/jni/hello-exe.c
  #include <stdio.h>
  int main(int argc, char ** argv) {
  printf("Hello, world!\n");
  return 0;
  }

## Slide 150: Make Execute File
Make Android.mk
  jni/Android.mk
  LOCAL_PATH := $(call my-dir)
  include $(CLEAR_VARS)
  LOCAL_MODULE := hello-exe
  LOCAL_SRC_FILES := hello-exe.c
  include $(BUILD_EXECUTABLE)

## Slide 151: Build Execute File
Build C/C++ Source Codes
Setup & Execute Execute File
      Required “root permission”
  ndk-build [clean all]
  adb push obj/local/armeabi/hello-exe /bin/
  adb shell
  $ cd bin
  $ chmod +x hello-exe
  ./hello-exe

## Slide 152: Setup Exe File with OTA-Build
init.*.rc in Nexus7(2013)
  ~/nexus_work/android/device/asus/flo/init.flo.rc
Copy your program to OTA-Package
  ~/nexus_work/android/build/target/product/mini.mk
    PRODUCT_COPY_FILES += \
    [local program path]:[system path]
  Ex.
    PRODUCT_COPY_FILES += \
    external/myapp/bin/myapp:system/usr/bin/myapp

## Slide 153: Init Script on Android
init.*.rc
  Auto Run on Boot Format:
    service [program name] [program path] [program option]…
      [service option]
      .
    Ex:
      service irsc_util /system/bin/logwrapper /system/bin/irsc_util "/etc/sec_config"
        class main <- service group
        user root <- run user or [group xxx]
        oneshot <- run once
  Change user/group/permission
    chown/chmod
    Ex:
      chmod 0777 /bin/myapp

## Slide 154: Boot Up Flow Kernel～Android System
Init
  Set Permission
  Mount Disks
  Load Driver
Demons
  Linux App
Zygote
  Sharing JavaResource Manager
Runtime
  Linux SO
  Driver

## Slide 155: Appendix: How to Setup so File
If you want to use your so file.
How to Setup:
  Copy so file to:
    PRODUCT_COPY_FILES += \
    external/myso/bin/libmyso.so:system/lib/libmyso.so
How to Use:
  With NDK. In “Android.mk”:
    LOCAL_LDLIBS := -lmyso